Hardware Requirements Specification

Plantation Productions Open Source/Open Hardware Data Acquisition System

Table of Contents

1	Introduction	4

1.1	System Purpose	4

1.2	Scope	4

1.3	Intended Audience	5

1.4	Definitions, Acronyms and Abbreviations	5

1.4.1	Definitions	5

1.4.2	Acronyms and Abbreviations	5

1.5	Existing Solutions	6

1.6	Argument for an Open-Source/Open-Hardware Solution	6

1.7	Overview/Contents of the Document	7

1.8	Document Conventions	7

2	General System Description	9

2.1	Design Basis	9

2.2	System Context	9

2.2.1	Digital Data Acquisition Control and Communications (CPU Interface)	9

2.2.2	Digital Inputs	10

2.2.3	Optically Isolated Digital Inputs	10

2.2.4	Digital Outputs	10

2.2.5	Analog Inputs	10

2.2.6	Analog Input Conditioning	10

2.2.7	Analog Outputs	11

2.2.8	Analog Output Conditioning	11

2.3	I/O Scanning	12

2.4	Analog Conditioning Adjustment	12

2.5	Host Communication	13

2.6	System Regulatory Issues	13

2.7	User Characteristics	13

3	Hardware Requirements	15

3.1	Hardware Requirements	15

3.1.1	CPU Interface Board (DAQIF)	15

3.1.2	Parallel I/O Interface Board (PPDIO96)	26

3.1.3	12-Channel Optoisolator Parallel Input Board (PPOPTO-12)	38

3.1.4	16-Channel Solid-State Relay Output Board (PPSSR16)	43

3.1.5	12-Channel Mechanical Relay Output Board (PPRELAY12)	51

3.1.6	48-Channel Digital Output Board (PPDO-48)	57

3.1.7	8-Channel Analog Input/4-Channel Analog Output Board (PPAIO-16/4)	62

3.1.8	PPAC-4 4-Channel Analog Conditioning Board	73

3.1.9	12-Channel Relay-based Digital I/O Board (PPRlyio-12)	75

3.1.10	PPAC420 4-20mA Analog Input Conditioning Board	91

3.2	System Operations	92

3.2.1	Human Factors	92

4	System Interfaces	93

4.1	Input Power	93

4.1.1	PPDAQ Input Power	93

4.1.2	PPAC4 Input Power	93

4.1.3	PPAIO16-4 Input Power	93

4.1.4	PPDIO96 Input Power	93

4.1.5	PPOPTO12 Input Power	93

4.1.6	PPRELAY Input Power	93

4.1.7	PPSSR16 Input Power	93

4.1.8	Netburner Input Power	93

4.1.9	Netburner Input Power -- USB	93

4.1.10	Ethernet Connection	93

4.1.11	RS-232 Serial Connection	93

4.1.12	USB Connection	94

# Introduction

This document is the Hardware Requirements Specification (HRS) for the Plantation Productions' Open Source/Open Hardware digital data acquisition system. The system hardware is covered under the Creative Commons (CC BY 4.0) found here:

https://creativecommons.org/licenses/by/4.0/

For the purposes of attribution, all work must be attributed to "Randall Hyde, Plantation Productions, Inc., Copyright 2016"

The Plantation Productions' digital data acquisition system consists of a series of modules (each with their own set of documentation) that provides the following functionality:

- Interface to some CPU module  (typically a SBC such as a Netburner MOD54415, Raspberry Pi 3, or Teensy 3.2, although the requirements do not limit the interface to these particular computers)

- A watchdog timer module to ensure correct system operation

- A digital input module accepting TTL (5V) or dry contact inputs

- An opto-isolation digital input interface that connects with the digital input module

- A digital output module featuring mechanical relays

- A digital output module featuring DC solid-state relays

- An analog I/O module featuring ADC and DAC components

- An analog input conditioning module that converts instrumentation analog levels (±10V) to voltage levels acceptable to the ADC module

- An analog input conditioning module that converts 4-20mA signals to voltage levels acceptable to the ADC module

- An analog output conditioning module that converts the DAC signals to instrument-level voltages (±10V)

This is not an inclusive list. Additional modules may be added to the system at a later date. Examples might include thermocouple or RTD input modules.

The CPU module will provide an interface to a general-purpose computer system (e.g., PC) via Ethernet, USB, or RS-232 serial; not all interfaces are required to support all three data transmission protocols. The system will employ the same communications protocol regardless of the physical interface.

The end result is a single well-documented and well-tested design that is applicable to the nuclear industry for data acquisition, output, and control.

## System Purpose

The purpose of the system is to provide an open, flexible, digital data acquisition system that can be incorporated into nuclear reactor control systems.

## Scope

The DAQ hardware and software will be produced from this specification.

The objectives of the hardware and software development are to provide functions, status information, monitor and control hardware, communications, internal and self-test functions per the requirements that have been allocated to the DAQ system.

## Intended Audience

The intended audience of this specification is the engineering, product assurance and management personnel involved in Plantation Productions' DAQ hardware and software development.

## Definitions, Acronyms and Abbreviations

### Definitions

The definitions used herein are consistent with IEEE 610.12-1990 with the following clarifications:

| Accuracy | The degree of agreement with the true value of the measured input, expressed as percent of reading for digital readouts. (ANSI N42.18-1980) |
| --- | --- |
| Anomaly | Anything observed in the documentation or operation of software that deviates from expectations. [Derived from IEEE Std 610.12-1990] |
| Catastrophic event | A catastrophic event is an event without warning from which recovery is impossible. Catastrophic events include hardware or software failures resulting in computation and processing errors The processor will halt or reset, based on a configuration item, after a catastrophic event. |
| Channel | The features and capabilities associated with a detector, a sensor, or a calculated group of information. |
| CPU | Central Processing Unit; specifically, a microcomputer chip. |
| Failsafe Condition | Failsafe condition is an actuated state of the TRIGA System as the result of a catastrophic failure such as loss of power, break of circuit or device failure catastrophic event |
| Handled Conditions | Conditions that the system is designed to handle and continue processing. These conditions include anomalies, faults and failures. |
| Hardware Requirements Specification | A specification that documents the hardware requirements (HRS) |
| Power Failure | Power failure is the condition when AC power is outside required limits or logic power is below a low limit. |
| Precision (per ANSI N42.18-80) | The degree of agreement of repeated measurements of the same input, expressed as percent deviation from the mean reading at 95% confidence level. |
| SBC | Single-board computer |
| Software Requirements Specification (SRS) | Documentation of the essential requirements (functions, performance, design constraints, and attributes) of the software and its external interfaces. [IEEE Std 610.12-1990] |
| System Requirements Specification (SyRS) | A structured collection of information that embodies the requirements of the system. [IEEE Std 1233-1998] A specification that documents the requirements to establish a design basis and the conceptual design for a system or subsystem. [GA-ESI] |

### Acronyms and Abbreviations

The abbreviations listed have the following meanings where used in this specification:

| AC | Alternating Current |
| --- | --- |
| ANSI | American National Standards Institute |
| CPU | Central Processing Unit |
| Cpm | Counts per Minute |
| DAQ | Data Acquisition (System) |
| DPDT | Double-Pole Double-Throw |
| FAT | Factory Acceptance Test |
| IEEE | Institute of Electrical and Electronic Engineers |
| LED | Light-Emitting Diode |
| MTBF | Mean Time between Failures |
| NEMA | National Electrical Manufacturers Association |
| NRC | Nuclear Regulatory Commission |
| RAM | Radiation Area Monitor |
| Rms | Root Mean Square |
| SyRS | System Requirements Specification |
| Vac | Voltage Alternating Current |
| Vdc | Voltage Direct Current |
| WDT | Watchdog Timer |

## Existing Solutions

Existing solutions have either been ad-hoc custom designs or have used common-off-the-shelf (COTS) devices. COTS devices have the following drawbacks:

- Support: COTS devices have a lifetime that is much shorter than a typical device installation at a nuclear reactor. Obtaining replacement parts becomes difficult after end-of-life occurs on the device.

- Proprietary: COTS devices often employ a proprietary design and/or proprietary firmware making it difficult to perform a safety analysis on such devices or ensure that the device meets system requirements.

- Communication protocol: many COTS devices use a proprietary communication protocol making it difficult to substitute a different device, should that become necessary (e.g., when a device reaches end-of-life).

Custom data acquisition designs also have drawbacks:

- Custom designs are very expensive.

- Custom designs require considerable engineering resources and time that may not be available.

- Custom designs require considerable cross-disciplinary support (e.g., software, hardware, and quality assurance); such resources may not be available at a given site.

- Custom designs are difficult to share with other sites, thus limiting the amortization of costs to a single reactor site.

## Argument for an Open-Source/Open-Hardware Solution

An open-source/open-hardware digital data acquisition solution offers several advantages over COTS and custom solutions. Some of the advantages include:

- Development costs are amortized across multiple installations (versus custom designs where the expense is applied to a single site).

- Once the design exists, the number of engineering resources is reduced as most of the low-level design work has already been done.

- Open designs have a much longer lifetime that COTS designs. As parts become obsolete an open design allows minimal re-engineering to replace just the parts that are obsolete without a huge impact on the overall design.

- Open designs use an open communication protocol and underlying hardware/software design. This makes is possible to perform system analysis to ensure that the system operates properly.

One other aspect of an open design is that it must be extensible. No single data acquisition system will be suitable for all reactor sites. The number of I/O channels (analog and digital) vary greatly from site to site. Although one could adopt a "one size fits all" solution where the design implements the maximum number of I/O channels handled at any site, this may present other problems (such as size or power restrictions). A better solution is to allow a system designer to build a system from a set of I/O modules and add additional modules for larger systems (or use fewer modules for smaller systems).

## Overview/Contents of the Document

The general description including product perspective, product functions, user characteristics and general constraints is included in Section 2.

The specific requirements including external interface requirements, system features, performance requirements, and other requirements are included in Section 3.  The system features are specified.  For each system feature, an introduction is provided and the details for each stimulus/response are provided.

The traceability (reverse traceability) to other documents (e.g., SyRS, SRS, SDD, HTC, HTP, STC, and STD) is documented in a separate document (Excel spreadsheet).

Section 2 contains the general description of the DAQ hardware and software.

The general description including product perspective, product functions, user characteristics and general constraints is included in this section.

Section 3 contains the specific requirements for the DAQ hardware.

The specific requirements including external interface requirements, system features, performance requirements, and other requirements are included in this section.

Section 4 contains other requirements or design goals

These are items that are not directly hardware related (that is, that derived from hardware design elements).

## Document Conventions

All system requirement tags shall take the form:

<whitespace>	[DAQ_HRS_xxx_yyy]

<whitespace>	[DAQ_HRS_xxx_yyy.zz]

<whitespace>	[DAQ_HRS_xxx_yyy.zz.aa]

etc.

where "xxx" is a three-digit SyRS requirement number and "yyy" is a three- or four-digit HRS requirement number.

For HRS requirement tags, should the need arise to insert a new HRS requirement tag between two other values (e.g., add a requirement between DAQ_HRS_030_040 and DAQ_HRS_030_041) then a decimal fractional number with exactly two digits shall be appended to the HRS tag number (e.g., DAQ_HRS_030_040.05). Any number of decimal point suffixes can be added, if needed (e.g., DAQ_HRS_030_40.05.02).

# General System Description

## Design Basis

The design basis for the DAQ System (or just "System") is to provide a system that can be verified to be correct as per regulatory requirements (e.g., NRC requirements).

## System Context

For the purposes of this HRS, the General System Description is laid out as:

- Digital data acquisition control and communications (CPU Interface)

- Digital input

- Digital output

- Analog input

- Analog output

### Digital Data Acquisition Control and Communications (CPU Interface)

The CPU interface module shall have the following responsibilities:

- Reading data from the digital and analog input devices

- Writing data to the digital and analog output devices

- Refreshing the watchdog timer

- Communicating with a host computer via Ethernet, USB, or RS-232 serial communication

The data acquisition and output modules shall communicate with a CPU via I2C and SPI communication busses and eight digital I/O lines (all 5V logic). In theory, you can interface any CPU or SBC that provides these I/O capabilities with the data acquisition and output modules. In practice, many CPUs/SBCs require additional logic-level shifting (e.g., between 3.3V and 5V) and an I2C expansion module, so the DAQ System will normally use a CPU interface board as an interface between the SBC/CPU and the data acquisition modules.

The CPU interface board is also a good place to put the watchdog timer circuitry.

The current CPU Interface board supports the Netburner MOD54415 MOD-DEV-70 evaluation board module, the Raspberry Pi 3 (any 40-pin Raspberry Pi module should also work), or a Teensy 3.2 module (high-performance Arduino-type board). The Netburner MOD-DEV-70 is the preferred SBC as it provides a true RTOS and Ethernet support (The Raspberry Pi is not real-time and the Teensy doesn't [directly] support Ethernet).

The existing CPU interface board also provides RS-232 level-shifting circuitry for the Teensy and Raspberry Pi SBCs (the Netburner provides this capability on-board, and doesn't use the circuitry on the CPU interface board).

Finally, the CPU interface board provides headers to connect with the various I/O modules using standard ribbon cabling.

Note: The Netburner and Teensy modules provide device-type USB support. To the host computer, these USB devices look like (very high speed) serial ports. Therefore, the host computer software actually sees only two types of devices: Ethernet and Serial, even though the System communicates with the host via USB, Ethernet, or RS-232 serial. Although the Raspberry Pi 3 SBC provides USB ports, these are all USB-host ports and cannot directly connect to the host computer system.  At this time, this specification ignores any USB ports (host or device) found on the Raspberry Pi SBCs.

### Digital Inputs

The System shall provide a minimum of 96 digital (TTL/5V) digital inputs with an expansion to more than 400 digital inputs as an option. By adding a pull-up resistor to +5V, these inputs should also be capable of reading dry contact switch inputs.

### Optically Isolated Digital Inputs

The System shall provide the ability to isolate groups of digital inputs via opto-isolation. The opto-isolation circuitry will sit between the input device(s) and the digital input circuitry. The opto-isolator units shall accept voltage levels in the range 0-15V (programmable by changing a resistor) or dry contact inputs. All digital inputs shall be isolated from one another as well as from the DAQ System digital inputs.

### Digital Outputs

The System shall provide a minimum of 12 digital outputs, expandable to at least 96 digital outputs. These digital outputs can be TTL/5V logic outputs, higher-current TTL/5V outputs (at least 50mA/output), mechanical relay outputs, solid-state relay outputs, or any combination of these three. Mechanical relay outputs will, at a minimum, support normally-open contacts; if possible, they should support normally-closed and normally-open contacts. Relays (solid-state or mechanical) should be fail-safe normally open. That is, when power is not applied or the System is not initialized, the relays should be in the "off" (open) position. This requirement does not apply to TTL outputs.  Note: the TTL output requirement can be realized by the digital input module if the digital inputs support a selectable "data direction" allowing the digital I/O bits to be programmed as either an input or an output bit. In such cases, the digital input module shall default to input on reset/power up.

### Analog Inputs

The System shall provide a minimum of 16 single-ended or 8 double-ended (differential) analog inputs. It should be expandable to a minimum of 64 single-ended or 32 double-ended analog inputs. The ADCs should provide a minimum of 12 bits of precision (signed, two's complement value), 16-bits is preferred. At the very least, the ADC inputs should be capable of handling 0-5V; any other analog inputs must be preprocessed by analog conditioning circuitry.

### Analog Input Conditioning

Separate (from the analog input) analog conditioning circuitry shall be capable of handling ±10V inputs and translating this to the voltage range acceptable to the ADC (e.g., 0-5V). The signal conditioning circuitry shall produce a differential output to be fed into the double-ended inputs on the ADC.

Separate analog signal conditioning circuitry shall be capable of translating a 4-20mA signal to the voltage range acceptable by the ADC (single-ended or differential inputs).

### Analog Outputs

The System shall provide a minimum of 4 analog outputs. It should be expandable to a minimum of 32 analog outputs. The DACs should provide a minimum of 12 bits of precision (signed, two's complement value). At the very least, the DAC inputs should be capable of producing 0-5V; any other analog inputs must be preprocessed by analog output conditioning circuitry.

### Analog Output Conditioning

Separate (from the analog output) analog conditioning circuitry shall be capable of converting the 0-5V output from the DAC to a range more acceptable to the System. Specifically, the analog output conditioning circuitry shall produce ±5V or ±10V when fed a 0-5V signal (note that 2.5V on input shall produce 0V on output).

#### CPU Interface Board

The data acquisition and output modules shall communicate with a CPU via I2C and SPI communication busses and eight digital I/O lines (all 5V logic). In theory, you can interface any CPU or SBC that provides these I/O capabilities with the data acquisition and output modules. In practice, many CPUs/SBCs require additional logic-level shifting (e.g., between 3.3V and 5V) and an I2C expansion module, so the DAQ System will normally use a CPU interface board as an interface between the SBC/CPU and the data acquisition modules.

The CPU interface board is also a good place to put the watchdog timer circuitry.

The current CPU Interface board supports the Netburner MOD54415 MOD-DEV-70 evaluation board module, the Raspberry Pi 3 (any 40-pin Raspberry Pi module should also work), or a Teensy 3.2 module (high-performance Arduino-type board). The Netburner MOD-DEV-70 is the preferred SBC as it provides a true RTOS and Ethernet support (The Raspberry Pi is not real-time and the Teensy doesn't [directly] support Ethernet).

The existing CPU interface board also provides RS-232 level-shifting circuitry for the Teensy and Raspberry Pi SBCs (the Netburner provides this capability on-board, and doesn't use the circuitry on the CPU interface board).

Finally, the CPU interface board provides headers to connect with the various I/O modules using standard ribbon cabling.

## I/O Scanning

The System shall periodically scan all the input devices and save the data for use by the host computer. During the scanning period, it shall also output any data received from the host computer. Note that the saved output data shall be written to the output devices (analog and digital) even if those values haven't been changed by the host computer since the last output cycle.

The I/O scanning period shall be no less than 25 msec and no more than 50 msec.

The System shall maintain a "history list" of 40 input readings since the last I/O request from the host. The list is a FIFO list; if the list overflows before the host reads the data, then the oldest readings are forgotten. Whenever the host reads the data, the System clears the list except for the most recent reading. If the inputs change in this list prior to reading the data, the System shall return data values (on an input-by-input basis) using one of the following mechanisms:

Digital:

- Most recent reading in history list

- First reading in history list

- Vote: the returned value is the largest number of zeros or ones (if there is a tie, the most recent reading wins).

- Loser: the returned value is the lesser number of zeros or ones (if there is a tie, the most recent reading wins).

- Debounce: the returned value is the longest sequence (with a minimum length specified by the host computer for the input) of a single value in the list. If no such sequence exists, the System returns the previous debounced value. If two or more sequences exist, the System returns the value of the most recent sequence).

Analog:

- Most recent reading in history list

- First reading in history list

- Minimum: smallest value in list

- Maximum: largest value in last

- Median: the middle value in a sorted version of the list

- Mean: arithmetic average of all values in the list

- Filtered: arithmetic average ignoring values outside a standard deviation value specified by host

## Analog Conditioning Adjustment

The analog conditioning circuitry (±10V to ADC input voltage) shall provide the following adjustments for each channel (typically using a potentiometer):

- Zero: sets the offset voltage for the conversion (adjusts the "zero" voltage for the analog conditioning output).

- Span: sets the gain of the analog conditioning circuitry.

- VRef: sets the voltage reference for the single-ended to double-ended conversion. Note that the double-ended ADC inputs may only support voltages in the range 0-5V. Negative voltages are converted to a double-ended signal where the actual value is represented by two voltage inputs (both in the range 0-5V, Vp and Vn) where the resulting value is computed as (Vp-Vn). The VRef input determines the value where Vp=Vn to produce a zero result. This is different from the ZERO adjustment, which sets the input voltage offset.

## Host Communication

The System software shall communicate with the host computer using one of two different protocols: the DIS64 protocol or the PPDAQ protocol.

The DIS64 protocol is a legacy protocol compatible with the DIS64 (Digital Input Scanner, 64 bits) board found in older General Atomics digital console systems. This protocol provides a drop-in replacement for these obsolete boards in legacy systems. Note that the DIS64 protocol communicates over RS-232 serial at 9600 bits per second, no parity, and one stop bit (as per the DIS64 board). The DIS64 protocol is only implemented via the Teensy 3.2 computer module (to save space and development effort, which is important consider the small audience for this particular protocol). The DIS64 protocol is for legacy systems only, newer designs should not use this protocol.

The PPDAQ protocol is the "standard" communication protocol for the System. This protocol communicates with the host via the Ethernet, USB, or RS-232 Serial ports. This protocol is a human-readable ASCII-text protocol with each command consisting of a sequence of ASCII characters terminated by a new line sequence ("\n" – the line feed character). The exact form of the protocol appears in the SRS document.

## System Regulatory Issues

Although the DAQ System has been designed with modern hardware and software engineering principles in mind – with an eye towards achieving approval from appropriate governmental regulatory agencies – the installing site has the ultimate responsibility for ensuring that the DAQ System meets their needs and is in compliance with whatever regulations may apply.

Although each site is responsible for achieving approval for the use of the DAQ System, the hope is that the approval process will be reduced in scope as different sites can share their experiences getting the DAQ System approved at their site.

## User Characteristics

In general, there are three types of individuals who use the DAQ System: end users, technicans, and system engineers.

- System engineers are those who design the DAQ System into their particular reactor control system and are responsible for testing and verifying the proper operation of the DAQ System at their installation.

- Technicians are those who are responsible for maintaining and calibrating the DAQ System after it is installed at their site.

- End users are reactor operators who use the DAQ System (indirectly) whenever they operate the reactor. Note that reactor operators may be blissfully unaware that the DAQ System hardware even exists. The DAQ System hardware could be replaced (it it could replace older hardware) and the end-user may not even be aware of the change.

There is no requirement that these three types of people all be different. The system engineer could also be responsible for on-going maintenance and calibration and could also be a reactor operator (end user).

# Hardware Requirements

## Hardware Requirements

### CPU Interface Board (DAQIF)

#### Netburner MOD54415 DEV-70 Evaluation Board Support

[DAQ_HRS_050_000]

The DAQIF board shall allow the connection of a Netburner MOD54415 (J2 Connector).

#### Raspberry Pi 3 Support

[DAQ_HRS_051_000]

The DAQIF board shall allow the connection of a Raspberry Pi 3 (GPIO Connector).

#### Teensy 3.2 Support

[DAQ_HRS_052_000]

The DAQIF board shall allow the connection of a Teensy 3.2 SBC (socket provided for headers on Teensy 3.2).

#### Single CPU Connection

[DAQ_HRS_053_000]

The DAQIF board shall only support the connection of a single CPU board (Netburner, Pi, or Teensy).

#### 5V Logic Levels

[DAQ_HRS_054_000]

The DAQIF board shall translate all voltage levels from the CPU boards to a 5V/TTL-compatible logic before such signals exit (or enter) the DAQIF.

Note: Some 3.3V output signals need not be converted as 3.3V outputs are TTL-logic compatible.

Note: I2C and SPI signals must be translated beween 3.3V and 5V before leaving the board.

[DAQ_HRS_054_001]

The DAQIF board shall translate the MOSI signal to a 5V/TTL-compatible logic level.

[DAQ_HRS_054_002]

The DAQIF board shall translate the MISO signal to a 5V/TTL-compatible logic level.

[DAQ_HRS_054_003]

The DAQIF board shall translate the SPI-CLK signal to a 5V/TTL-compatible logic level.

[DAQ_HRS_054_004]

The DAQIF board shall translate the IRQ signal to a 5V/TTL-compatible logic level.

[DAQ_HRS_054_005]

The DAQIF board shall translate the RESET signal to a 5V/TTL-compatible logic level.

[DAQ_HRS_054_006]

The DAQIF board shall translate the J2_38 signal to a 5V/TTL-compatible logic level.

[DAQ_HRS_054_007]

The DAQIF board shall translate the WD_LATCH signal to a 5V/TTL-compatible logic level.

[DAQ_HRS_054_008]

The DAQIF board shall translate the SDA signal to a 5V/TTL-compatible logic level.

[DAQ_HRS_054_009]

The DAQIF board shall translate the SCL signal to a 5V/TTL-compatible logic level.

#### TTL Fanout

[DAQ_HRS_055_000]

All logic output signals from the DAQIF board shall support a TTL fanout of at least 10. (Buffer chips required if a particular signal has a fanout of less than 10.)

[DAQ_HRS_055_001]

The MOSI5 signal shall support a TTL fanout of at least 10.

[DAQ_HRS_055_002]

The SPI-CLK signal shall support a TTL fanout of at least 10.

[DAQ_HRS_055_003]

The WD_LATCH signal shall support a TTL fanout of at least 10.

[DAQ_HRS_055_004]

The RESET signal shall support a TTL fanout of at least 10.

#### SPI Chip/Board Select Expansion

[DAQ_HRS_056_000]

The DAQIF shall provide an SPI chip select expansion (74HC138) with 8 chip selects (BS0-BS7).

[DAQ_HRS_056_001]

The DAQIF connects one CPU output pin to the "A" address pin on the 74HC138.

Note: pin shall be labelled "A0" in schematic.

[DAQ_HRS_056_002]

The DAQIF connects one CPU output pin to the "B" address pin on the 74HC138.

Note: pin shall be labelled "A1" in schematic.

[DAQ_HRS_056_003]

The DAQIF connect one CPU output pin to the "C" address pin on the 74HC138.

Note: pin shall be labelled "A2" in schematic.

[DAQ_HRS_056_004]

The DAQIF shall connect one CPU output pin to the "G2A" enable pin on the 74HC138.

Note: pin shall be labelled "SPI-CS" in schematic.

[DAQ_HRS_056_005]

Writing (1,0,0,0) to the 74HC138 (A0, A1, A2, G2A) lines will activate (active low) BS1 on the PPDIO96 connector.

[DAQ_HRS_056_006]

Writing (1,0,0,0) to the 74HC138 (A0, A1, A2, G2A) lines will deactivate all SPI chip selects except BS1 on the PPDIO and PPDIO96 connectors.

[DAQ_HRS_056_007]

Writing (0,1,0,0) to the 74HC138 (A0, A1, A2, G2A) lines will activate (active low) BS2 on the PPDIO96 connector.

[DAQ_HRS_056_008]

Writing (0,1,0,0) to the 74HC138 (A0, A1, A2, G2A) lines will deactivate all SPI chip selects except BS2 on the PPDIO and PPDIO96 connectors.

[DAQ_HRS_056_009]

Writing (1,1,0,0) to the 74HC138 (A0, A1, A2, G2A) lines will activate (active low) BS3 on the PPDIO96 connector.

[DAQ_HRS_056_010]

Writing (1,1,0,0) to the 74HC138 (A0, A1, A2, G2A) lines will deactivate all SPI chip selects except BS3 on the PPDIO and PPDIO96 connectors.

[DAQ_HRS_056_011]

Writing (0,0,1,0) to the 74HC138 (A0, A1, A2, G2A) lines will activate (active low) BS4 on the PPDIO96 connector.

[DAQ_HRS_056_012]

Writing (0,0,1,0) to the 74HC138 (A0, A1, A2, G2A) lines will deactivate all SPI chip selects except BS4 on the PPDIO and PPDIO96 connectors.

[DAQ_HRS_056_013]

Writing (1,0,1,0) to the 74HC138 (A0, A1, A2, G2A) lines will activate (active low) BS5 on the PPDIO96 connector.

[DAQ_HRS_056_014]

Writing (1,0,1,0) to the 74HC138 (A0, A1, A2, G2A) lines will deactivate all SPI chip selects except BS5 on the PPDIO and PPDIO96 connectors.

[DAQ_HRS_056_015]

Writing (0,1,1,0) to the 74HC138 (A0, A1, A2, G2A) lines will activate (active low) BS6 on the PPDIO96 connector.

[DAQ_HRS_056_016]

Writing (0,1,1,0) to the 74HC138 (A0, A1, A2, G2A) lines will deactivate all SPI chip selects except BS6 on the PPDIO and PPDIO96 connectors.

[DAQ_HRS_056_017]

Writing 1 to the 74HC138 G2A line will deactivate all SPI chip selects on the PPDIO and PPDIO96 connectors.

#### Reserved SPI Chip Select

[DAQ_HRS_057_000]

The DAQIF shall reserve BS7 (chip select #8) for "nothing selected".

[DAQ_HRS_057_001]

Writing (1,1,1,0) to the 74HC138 (A0, A1, A2, G2A) lines will deactivate all SPI chip selects on the PPDIO and PPDIO96 connectors.

#### Serial Output SPI Chip Select

[DAQ_HRS_058_000]

The DAQIF shall reserve BS0 (chip select #1) for a special serial output bus.

[DAQ_HRS_058_001]

Writing (0,0,0,0) to the 74HC138 (A0, A1, A2, G2A) lines will activate (active low) BS0 on the PPDO connector.

[DAQ_HRS_058_002]

Writing (0,0,0,0) to the 74HC138 (A0, A1, A2, G2A) lines will deactivate all SPI chip selects except BS0 on the PPDIO and PPDIO96 connectors.

#### Parallel Input SPI Chip Selects

[DAQ_HRS_059_000]

The DAQIF shall reserve BS1-BS6 (chip selects #2-#7) for accessing PPDIO96 parallel I/O boards.

#### I2C Expansion

[DAQ_HRS_060_000]

The DAQIF shall provide an I2C expansion facility to expand a single I2C port to 8 I2C ports.

#### Application-Defined I/O Pin

[DAQ_HRS_060_001]

The DAQIF shall provide an I/O pin reserved for application purposes.

Note: the schematic shall use the label "J2_38" for this pin.

#### Watchdog Timer

[DAQ_HRS_061_000]

The DAQIF shall provide watchdog timer to monitor software operation.

#### Watchdog Timeout Period

[DAQ_HRS_062_000]

The DAQIF watchdog timeout period shall be between 2 and 10 seconds (nominally 5 seconds).

#### Watchdog Latch

[DAQ_HRS_063_000]

The DAQIF shall latch the watchdog timeout output until the CPU explicitly resets it.

#### Watchdog Feedback

[DAQ_HRS_064_000]

The DAQIF watchdog timeout signal shall be made available to the CPU module.

#### Watchdog Reset

[DAQ_HRS_065_000]

The CPU module shall provide a digital output line (RESET) that will reset the DAQIF watchdog trip.

Note: this reset line may be shared with other reset functions.

#### Watchdog Timeout Reset

[DAQ_HRS_066_000]

The CPU module shall provide a digital output line (WD_RFSH) that will reset the DAQIF watchdog timeout period.

#### Watchdog Relay

[DAQ_HRS_067_000]

The DAQIF shall provide an SPDT relay with normally open and normally closed contacts.

#### Watchdog Relay – Not Actuated

[DAQ_HRS_068_000]

The watchdog relay shall be unactuated (normally open contacts open, normally closed contacts closed) whenever the watchdog latch is not actuated.

#### Watchdog Relay – Actuated

[DAQ_HRS_069_000]

The watchdog relay shall be actuated (normally open contacts closed, normally closed contacts open) whenever the watchdog latch is actuated.

#### Watchdog LED

[DAQ_HRS_070_000]

The DAQIF shall provide an LED that illuminates whenever the watchdog latch is actuated.

#### Watchdog Output Connector

[DAQ_HRS_071_000]

The DAQIF shall provide a 3-pin header (0.1" centers) with the NC/COM/NO signals from the watchdog relay.

#### Power Supply LED

[DAQ_HRS_072_000]

The DAQIF shall provide an LED that is illuminated whenever power is applied to the board.

#### RS-232 Level Shifting

[DAQ_HRS_073_000]

The DAQIF shall provide level shifting from TTL levels to RS-232 levels.

Note: this functionality is only necessary for the Raspberry Pi and Teensy CPUs. The Netburner MOD54415 evaluation board already provides this functionality.

#### RS-232 DCE Connection

[DAQ_HRS_074_000]

The DAQIF shall provide a DB9F (female) connection with a DCE (data communications equipment) interface.

#### RS-232 DTE Connection

[DAQ_HRS_075_000]

The DAQIF shall provide a DB9 (male) connection with a DTE (data terminal equipment) interface.

Note: DTE is the standard connector for this type of device. DCE is provided to avoid a NULL modem connection when connecting directly to a terminal device such as a PC.

#### PPDO Connection

[DAQ_HRS_076_000]

The DAQIF shall provide a 10-pin header (2x5) to connect to serial output boards (e.g., PPSSR-16 and PPRELAY-12).

#### PPDO Signals

[DAQ_HRS_076_001]

The DAQIF shall provide a BS0 (board select zero) output signal on the PPDO connector.

Note: see [DAQ_HRS_058_001] and [DAQ_HRS_058_002] for BS0 action requirements.

[DAQ_HRS_076_002]

The DAQIF shall provide a 5V MISO (SPI Master In Slave Out) input signal on the PPDO connector.

[DAQ_HRS_076_003]

The DAQIF shall provide a 5V MOSI (SPI Master Out Slave In) output signal on the PPDO connector.

[DAQ_HRS_076_004]

The DAQIF shall provide a 5V SPI Clock output signal on the PPDO connector.

[DAQ_HRS_076_005]

The DAQIF shall provide a 5V application-defined I/O signal on the PPDO connector (J2_38).

[DAQ_HRS_076_006]

The DAQIF shall provide a 5V Reset signal output on the PPDO connector.

[DAQ_HRS_076_007]

The DAQIF shall provide a 5V Watchdog Latch output signal on the PPDO connector.

[DAQ_HRS_076_008]

The DAQIF shall provide a 5V IRQ input signal on the PPDO connector.

#### PPDO Connection Pinout

[DAQ_HRS_077_000]

The DAQIF PPDO connector shall use the following pinout:

[DAQ_HRS_077_001]

1: 		BS0 (SPI chip select #1)

[DAQ_HRS_077_002]

2:		VCC (+5V)

[DAQ_HRS_077_003]

3:		MISO (5V SPI master data in, slave data out)

[DAQ_HRS_077_004]

4:		MOSI (5V SPI master data out, slave data in)

[DAQ_HRS_077_005]

5:		CLK (5V SPI clock)

[DAQ_HRS_077_006]

6:		J2_38_5 (5V digital signal, reserved for future use)

[DAQ_HRS_077_007]

7:		Reset (5V logic reset signal – common with watchdog reset, used to reset serial latches).

[DAQ_HRS_077_008]

8:		Watchdog latch (5V signal indicates watchdog timeout).

[DAQ_HRS_077_009]

9:		IRQ (5V—open drain signal to the CPU indicating an interrupt condition)

[DAQ_HRS_077_010]

10:	Gnd

#### PPDIO96 Connection

[DAQ_HRS_078_000]

The DAQIF shall provide a 14-pin header (2x7) to connect to PPDIO96 parallel I/O boards (or signal-compatible devices).

#### PPDIO96 Signals

[DAQ_HRS_078_001]

The DAQIF shall provide a BS1 (board select zero) output signal on the PPDIO96 connector.

Note: see [DAQ_HRS_056_005] and [DAQ_HRS_056_006] for BS1 action requirements.

[DAQ_HRS_078_002]

The DAQIF shall provide a BS2 (board select zero) output signal on the PPDIO96 connector.

Note: see [DAQ_HRS_056_007] and [DAQ_HRS_056_008] for BS2 action requirements.

[DAQ_HRS_078_003]

The DAQIF shall provide a BS3 (board select zero) output signal on the PPDIO96 connector.

Note: see [DAQ_HRS_056_009] and [DAQ_HRS_056_010] for BS3 action requirements.

[DAQ_HRS_078_004]

The DAQIF shall provide a BS4 (board select zero) output signal on the PPDIO96 connector.

Note: see [DAQ_HRS_056_011] and [DAQ_HRS_056_012] for BS4 action requirements.

[DAQ_HRS_078_005]

The DAQIF shall provide a BS5 (board select zero) output signal on the PPDIO96 connector.

Note: see [DAQ_HRS_056_013] and [DAQ_HRS_056_014] for BS5 action requirements.

[DAQ_HRS_078_006]

The DAQIF shall provide a BS6 (board select zero) output signal on the PPDIO96 connector.

Note: see [DAQ_HRS_056_015]  and [DAQ_HRS_056_016] for BS6 action requirements.

[DAQ_HRS_078_007]

The DAQIF shall provide a 5V MISO (SPI Master In Slave Out) input signal on the PPDO connector.

[DAQ_HRS_078_008]

The DAQIF shall provide a 5V MOSI (SPI Master Out Slave In) output signal on the PPDO connector.

[DAQ_HRS_078_009

The DAQIF shall provide a 5V SPI Clock output signal on the PPDO connector.

[DAQ_HRS_078_010]

The DAQIF shall provide a 5V application-defined I/O signal on the PPDO connector (J2_38).

[DAQ_HRS_078_011]

The DAQIF shall provide a 5V Reset signal output on the PPDO connector.

[DAQ_HRS_078_012]

The DAQIF shall provide a 5V Watchdog Latch output signal on the PPDO connector.

[DAQ_HRS_078_013]

The DAQIF shall provide a 5V IRQ input signal on the PPDO connector.

#### PPDIO96 Connection Pinout

[DAQ_HRS_079_000]

The DAQIF  PPDIO96 connector shall use the following pinout:

[DAQ_HRS_079_001]

1:	J2_38_5 (5V digital signal, reserved for future use)

[DAQ_HRS_079_002]

2:	Watchdog latch (5V signal indicates watchdog timeout).

[DAQ_HRS_079_003]

3:	BS1 (SPI chip select #2)

[DAQ_HRS_079_004]

4:	Gnd

[DAQ_HRS_079_005]

5:	BS2 (SPI chip select #3)

[DAQ_HRS_079_006]

6:	MOSI (5V SPI master data out, slave data in)

[DAQ_HRS_079_007]

7:	BS3 (SPI chip select #4)

[DAQ_HRS_079_008]

8:	CLK (5V SPI Clock)

[DAQ_HRS_079_009]

9:	BS4 (SPI chip select #5)

[DAQ_HRS_079_010]

10:	MISO (5V SPI master data in, slave data out)

[DAQ_HRS_079_011]

11:	BS5 (SPI chip select #6)

[DAQ_HRS_079_012]

12:	IRQ (5V—open drain signal to the CPU indicating an interrupt condition)

[DAQ_HRS_079_013]

13:	BS6 (SPI chip select #7)

[DAQ_HRS_079_014]

14:	Reset (5V logic reset signal – common with watchdog reset, used to reset serial latches).

Note: BSn signals need to be TTL compatible; they could be 3.3V or 5V signals.

#### I2C Connections

[DAQ_HRS_080_000]

The DAQIF shall have four 6-pin (2x3) headers, each of which provides two I2C connections from the I2C expander.

#### I2C Connector Pinouts

[DAQ_HRS_081_000]

The DAQIF  I2C connections shall use the following pinouts:

Connector 0/1:

[DAQ_HRS_081_001]

1:	SD0 (5V I2C port 0 data)

[DAQ_HRS_081_002]

2:	SD1 (5V I2C port 1 data)

[DAQ_HRS_081_003]

3:	SC0 (5V I2C port 0 clock)

[DAQ_HRS_081_004]

4:	SC1 (5V I2C port 1 clock)

[DAQ_HRS_081_005]

5:	Gnd

[DAQ_HRS_081_006]

6:	Gnd

Connector 2/3:

[DAQ_HRS_081_007]

1:	SD2 (5V I2C port 2 data)

[DAQ_HRS_081_008]

2:	SD3 (5V I2C port 3 data)

[DAQ_HRS_081_009]

3:	SC2 (5V I2C port 2 clock)

[DAQ_HRS_081_010]

4:	SC3 (5V I2C port 3 clock)

[DAQ_HRS_081_011]

5:	Gnd

[DAQ_HRS_081_012]

6:	Gnd

Connector 4/5:

[DAQ_HRS_081_013]

1:	SD4 (5V I2C port 4 data)

[DAQ_HRS_081_014]

2:	SD5 (5V I2C port 5 data)

[DAQ_HRS_081_015]

3:	SC4 (5V I2C port 4 clock)

[DAQ_HRS_081_016]

4:	SC5 (5V I2C port 5 clock)

[DAQ_HRS_081_017]

5:	Gnd

[DAQ_HRS_081_018]

6:	Gnd

Connector 6/7:

[DAQ_HRS_081_019]

1:	SD6 (5V I2C port 6 data)

[DAQ_HRS_081_020]

2:	SD7 (5V I2C port 7 data)

[DAQ_HRS_081_021]

3:	SC6 (5V I2C port 6 clock)

[DAQ_HRS_081_022]

4:	SC7 (5V I2C port 7 clock)

[DAQ_HRS_081_023]

5:	Gnd

[DAQ_HRS_081_024]

6:	Gnd

#### DAQIF Power Supply Connection

[DAQ_HRS_082_000]

The DAQIF shall provide a two-pin screw terminal connector (5mm centers) to accept 5V/Gnd from an external power supply

#### DAQIF 3.3V Power Supply

[DAQ_HRS_083_000]

The DAQIF shall provide on-board voltage regulation for any voltages other than the 5V provided on the power connection (e.g., 3.3V for many of the on-board logic chips).

### Parallel I/O Interface Board (PPDIO96)

#### PPDIO96 Capacity

[DAQ_HRS_150_000]

The PPDIO96 shall provide 96 bits of parallel I/O.

#### PPDIO96 I/O Expansion Chips

[DAQ_HRS_151_000]

The PPDIO96 shall use six MCP23S17 I/O expansion ICs (16 I/O pins per chip).

#### PPDIO96 Input Connection

[DAQ_HRS_152_000]

The PPDIO96 shall use the PPDIO96 data connection (2x7 pin header, see [DAQ_HRS_079_000]) as the input connector.

#### PPDIO96 Output Connection

[DAQ_HRS_153_000]

The PPDIO96 shall use the PPDIO96 data connection (2x7 pin header, see [DAQ_HRS_079_000]) as the output connector with the following changes:

[DAQ_HRS_153_001]

BS2 on input connector is routed to BS1 on output connector.

[DAQ_HRS_153_002]

BS3 on input connector is routed to BS2 on output connector.

[DAQ_HRS_153_003]

BS4 on input connector is routed to BS3 on output connector.

[DAQ_HRS_153_004]

BS5 on input connector is routed to BS4 on output connector.

[DAQ_HRS_153_005]

BS6 on input connector is routed to BS5 on output connector.

[DAQ_HRS_153_006]

BS6 on the output connector is tied to +5V.

#### PPDIO96 IRQ Connection

[DAQ_HRS_154_000]

The PPDIO96 shall provide a jumper connection for each MCP23S17 chip that allows the user to connect the chip's INTA pin to the IRQ pin on the PPDIO96 connector.

#### PPDIO96 I/O Connections

[DAQ_HRS_155_000]

The PPDIO96 shall provide eight 20-pin (2x10) headers connecting to the data pins on the MCP23S17 IC.

Note: this document refers to each of the connectors as a "bank".

#### PPDIO96 Bank 0 Pinout

[DAQ_HRS_156_000]

The PPDIO96 Bank 0 header shall use the following pinout:

[DAQ_HRS_156_001]

1:	Bit 1 (MCP23S17 #1 GPB6, bank 0:bit 1)

[DAQ_HRS_156_002]

2:	Bit 0 (MCP23S17 #1 GPB7, bank 0:bit 0)

[DAQ_HRS_156_003]

3:	Bit 2 (MCP23S17 #1 GPB5, bank 0:bit 2)

[DAQ_HRS_156_004]

4:	Gnd

[DAQ_HRS_156_005]

5:	Bit 3 (MCP23S17 #1 GPB4, bank 0:bit 3)

[DAQ_HRS_156_006]

6:	Gnd

[DAQ_HRS_156_007]

7:	Bit 4 (MCP23S17 #1 GPB3, bank 0:bit 4)

[DAQ_HRS_156_008]

8:	Gnd

[DAQ_HRS_156_009]

9:	Bit 5 (MCP23S17 #1 GPB2, bank 0:bit 5)

[DAQ_HRS_156_010]

10:	Gnd

[DAQ_HRS_156_011]

11:	Bit 6 (MCP23S17 #1 GPB1, bank 0:bit 6)

[DAQ_HRS_156_012]

12:	Gnd

[DAQ_HRS_156_013]

13:	Bit 7 (MCP23S17 #1 GPB0, bank 0:bit 7)

[DAQ_HRS_156_014]

14:	Gnd

[DAQ_HRS_156_015]

15:	Bit 8 (MCP23S17 #1 GPA7, bank 0:bit 8)

[DAQ_HRS_156_016]

16:	Gnd

[DAQ_HRS_156_017]

17:	Bit 9 (MCP23S17 #1 GPA6, bank 0:bit 9)

[DAQ_HRS_156_018]

18:	Gnd

[DAQ_HRS_156_019]

19:	Bit 10 (MCP23S17 #1 GPA5, bank 0:bit 10)

[DAQ_HRS_156_020]

20: 	Bit 11 (MCP23S17 #1 GPA4, bank 0:bit 11)

Note: Gnd pins are all connected to the same ground plane.

#### PPDIO96 Bank 1 Pinout

[DAQ_HRS_157_000]

The PPDIO96 Bank 1 header shall use the following pinout:

[DAQ_HRS_157_001]

1:	Bit 13 (MCP23S17 #1 GPA2, bank 1:bit 1)

[DAQ_HRS_157_002]

2:	Bit 12 (MCP23S17 #1 GPA3, bank 1:bit 0)

[DAQ_HRS_157_003]

3:	Bit 14 (MCP23S17 #1 GPA1, bank 1:bit 2)

[DAQ_HRS_157_004]

4:	Gnd

[DAQ_HRS_157_005]

5:	Bit 15 (MCP23S17 #1 GPA0, bank 1:bit 3)

[DAQ_HRS_157_006]

6:	Gnd

[DAQ_HRS_157_007]

7:	Bit 16 (MCP23S17 #2 GPB7, bank 1:bit 4)

[DAQ_HRS_157_008]

8:	Gnd

[DAQ_HRS_157_009]

9:	Bit 17 (MCP23S17 #2 GPB6, bank 1:bit 5)

[DAQ_HRS_157_010]

10:	Gnd

[DAQ_HRS_157_011]

11:	Bit 18 (MCP23S17 #2 GPB5, bank 1:bit 6)

[DAQ_HRS_157_012]

12:	Gnd

[DAQ_HRS_157_013]

13:	Bit 19 (MCP23S17 #2 GPB4, bank 1:bit 7)

[DAQ_HRS_157_014]

14:	Gnd

[DAQ_HRS_157_015]

15:	Bit 20 (MCP23S17 #2 GPB3, bank 1:bit 8)

[DAQ_HRS_157_016]

16:	Gnd

[DAQ_HRS_157_017]

17:	Bit 21 (MCP23S17 #2 GPB2, bank 1:bit 9)

[DAQ_HRS_157_018]

18:	Gnd

[DAQ_HRS_157_019]

19:	Bit 22 (MCP23S17 #2 GPB1, bank 1:bit 10)

[DAQ_HRS_157_020]

20:	Bit 23 (MCP23S17 #2 GPB0, bank 1:bit 11)

Note: Gnd pins are all connected to the same ground plane.

#### PPDIO96 Bank 2 Pinout

[DAQ_HRS_158_000]

The PPDIO96 Bank 2 header shall use the following pinout:

[DAQ_HRS_158_001]

1:	Bit 25 (MCP23S17 #2 GPA1, bank 2:bit 1)

[DAQ_HRS_158_002]

2:	Bit 24 (MCP23S17 #2 GPA0, bank 2:bit 0)

[DAQ_HRS_158_003]

3:	Bit 26 (MCP23S17 #2 GPA2, bank 2:bit 2)

[DAQ_HRS_158_004]

4:	Gnd

[DAQ_HRS_158_005]

5:	Bit 27 (MCP23S17 #2 GPA3, bank 2:bit 3)

[DAQ_HRS_158_006]

6:	Gnd

[DAQ_HRS_158_007]

7:	Bit 28 (MCP23S17 #2 GPA4, bank 2:bit 4)

[DAQ_HRS_158_008]

8:	Gnd

[DAQ_HRS_158_009]

9:	Bit 29 (MCP23S17 #2 GPA5, bank 2:bit 5)

[DAQ_HRS_158_010]

10:	Gnd

[DAQ_HRS_158_011]

11:	Bit 30 (MCP23S17 #2 GPA6, bank 2:bit 6)

[DAQ_HRS_158_012]

12:	Gnd

[DAQ_HRS_158_013]

13:	Bit 31 (MCP23S17 #2 GPA7, bank 2:bit 7)

[DAQ_HRS_158_014]

14:	Gnd

[DAQ_HRS_158_015]

15:	Bit 32 (MCP23S17 #3 GPB7, bank 2:bit 8)

[DAQ_HRS_158_016]

16:	Gnd

[DAQ_HRS_158_017]

17:	Bit 33 (MCP23S17 #3 GPB6, bank 2:bit 9)

[DAQ_HRS_158_018]

18:	Gnd

[DAQ_HRS_158_019]

19:	Bit 34 (MCP23S17 #3 GPB5, bank 2:bit 10)

[DAQ_HRS_158_020]

20:	Bit 35 (MCP23S17 #3 GPB4, bank 2:bit 11)

Note: Gnd pins are all connected to the same ground plane.

#### PPDIO96 Bank 3 Pinout

[DAQ_HRS_159_000]

The PPDIO96 Bank 3 header shall use the following pinout:

[DAQ_HRS_159_001]

1:	Bit 37 (MCP23S17 #3 GPB2, bank 3:bit 1)

[DAQ_HRS_159_002]

2:	Bit 36 (MCP23S17 #3 GPB3, bank 3:bit 0)

[DAQ_HRS_159_003]

3:	Bit 38 (MCP23S17 #3 GPB1, bank 3:bit 2)

[DAQ_HRS_159_004]

4:	Gnd

[DAQ_HRS_159_005]

5:	Bit 39 (MCP23S17 #3 GPB0, bank 3:bit 3)

[DAQ_HRS_159_006]

6:	Gnd

[DAQ_HRS_159_007]

7:	Bit 40 (MCP23S17 #3 GPA7, bank 3:bit 4)

[DAQ_HRS_159_008]

8:	Gnd

[DAQ_HRS_159_009]

9:	Bit 41 (MCP23S17 #3 GPA6, bank 3:bit 5)

[DAQ_HRS_159_010]

10:	Gnd

[DAQ_HRS_159_011]

11:	Bit 42 (MCP23S17 #3 GPA5, bank 3:bit 6)

[DAQ_HRS_159_012]

12:	Gnd

[DAQ_HRS_159_013]

13:	Bit 43 (MCP23S17 #3 GPA4, bank 3:bit 7)

[DAQ_HRS_159_014]

14:	Gnd

[DAQ_HRS_159_015]

15:	Bit 44 (MCP23S17 #3 GPA3, bank 3:bit 8)

[DAQ_HRS_159_016]

16:	Gnd

[DAQ_HRS_159_017]

17:	Bit 45 (MCP23S17 #3 GPA2, bank 3:bit 9)

[DAQ_HRS_159_018]

18:	Gnd

[DAQ_HRS_159_019]

19:	Bit 46 (MCP23S17 #3 GPA1, bank 3:bit 10)

[DAQ_HRS_159_020]

20:	Bit 47 (MCP23S17 #3 GPA0, bank 3:bit 1)

Note: Gnd pins are all connected to the same ground plane.

#### PPDIO96 Bank 4 Pinout

[DAQ_HRS_160_000]

The PPDIO96 Bank 4 header shall use the following pinout:

[DAQ_HRS_160_001]

1:	Bit 49 (MCP23S17 #4 GPB2, bank 4:bit 1)

[DAQ_HRS_160_002]

2:	Bit 48 (MCP23S17 #4 GPB3, bank 4:bit 0)

[DAQ_HRS_160_003]

3:	Bit 50 (MCP23S17 #4 GPB1, bank 4:bit 2)

[DAQ_HRS_160_004]

4:	Gnd

[DAQ_HRS_160_005]

5:	Bit 51 (MCP23S17 #4 GPB0, bank 4:bit 3)

[DAQ_HRS_160_006]

6:	Gnd

[DAQ_HRS_160_007]

7:	Bit 52 (MCP23S17 #4 GPA7, bank 4:bit 4)

[DAQ_HRS_160_008]

8:	Gnd

[DAQ_HRS_160_009]

9:	Bit 53 (MCP23S17 #4 GPA6, bank 4:bit 5)

[DAQ_HRS_160_010]

10:	Gnd

[DAQ_HRS_160_011]

11:	Bit 54 (MCP23S17 #4 GPA5, bank 4:bit 6)

[DAQ_HRS_160_012]

12:	Gnd

[DAQ_HRS_160_013]

13:	Bit 55 (MCP23S17 #4 GPA4, bank 4:bit 7)

[DAQ_HRS_160_014]

14:	Gnd

[DAQ_HRS_160_015]

15:	Bit 56 (MCP23S17 #4 GPA3, bank 4:bit 8)

[DAQ_HRS_160_016]

16:	Gnd

[DAQ_HRS_160_017]

20:	Bit 57 (MCP23S17 #4 GPA2, bank 4:bit 9)

[DAQ_HRS_160_018]

18:	Gnd

[DAQ_HRS_160_019]

19:	Bit 58 (MCP23S17 #4 GPA1, bank 4:bit 10)

[DAQ_HRS_160_020]

20:	Bit 59 (MCP23S17 #4 GPA0, bank 4:bit 11)

Note: Gnd pins are all connected to the same ground plane.

#### PPDIO96 Bank 5 Pinout

[DAQ_HRS_161_000]

The PPDIO96 Bank 5 header shall use the following pinout:

[DAQ_HRS_161_001]

1:	Bit 61 (MCP23S17 #5 GPA6, bank 5:bit 1)

[DAQ_HRS_161_002]

2:	Bit 60 (MCP23S17 #5 GPA7, bank 5:bit 0)

[DAQ_HRS_161_003]

3:	Bit 62 (MCP23S17 #5 GPA5, bank 5:bit 2)

[DAQ_HRS_161_004]

4:	Gnd

[DAQ_HRS_161_005]

5:	Bit 63 (MCP23S17 #5 GPA4, bank 5:bit 3)

[DAQ_HRS_161_006]

6:	Gnd

[DAQ_HRS_161_007]

7:	Bit 64 (MCP23S17 #5 GPA3, bank 5:bit 4)

[DAQ_HRS_161_008]

8:	Gnd

[DAQ_HRS_161_009]

9:	Bit 65 (MCP23S17 #5 GPA2, bank 5:bit 5)

[DAQ_HRS_161_010]

10:	Gnd

[DAQ_HRS_161_011]

11:	Bit 66 (MCP23S17 #5 GPA1, bank 5:bit 6)

[DAQ_HRS_161_012]

12:	Gnd

[DAQ_HRS_161_013]

13:	Bit 67 (MCP23S17 #5 GPA0, bank 5:bit 7)

[DAQ_HRS_161_014]

14:	Gnd

[DAQ_HRS_161_015]

15:	Bit 68 (MCP23S17 #4 GPB7, bank 5:bit 8)

[DAQ_HRS_161_016]

16:	Gnd

[DAQ_HRS_161_017]

17:	Bit 69 (MCP23S17 #4 GPB6, bank 5:bit 9)

[DAQ_HRS_161_018]

18:	Gnd

[DAQ_HRS_161_019]

19:	Bit 70 (MCP23S17 #4 GPB5, bank 5:bit 10)

[DAQ_HRS_161_020]

20:	Bit 71 (MCP23S17 #4 GPB4, bank 5:bit 11)

Note: Gnd pins are all connected to the same ground plane.

#### PPDIO96 Bank 6 Pinout

[DAQ_HRS_162_000]

The PPDIO96 Bank 6 header shall use the following pinout:

[DAQ_HRS_162_001]

1:	Bit 73 (MCP23S17 #6 GPA2, bank 6:bit 1)

[DAQ_HRS_162_002]

2:	Bit 72 (MCP23S17 #6 GPA3, bank 6:bit 0)

[DAQ_HRS_162_003]

3:	Bit 74 (MCP23S17 #6 GPA1, bank 6:bit 2)

[DAQ_HRS_162_004]

4:	Gnd

[DAQ_HRS_162_005]

5:	Bit 75 (MCP23S17 #6 GPA0, bank 6:bit 3)

[DAQ_HRS_162_006]

6:	Gnd

[DAQ_HRS_162_007]

7:	Bit 76 (MCP23S17 #5 GPB7, bank 6:bit 4)

[DAQ_HRS_162_008]

8:	Gnd

[DAQ_HRS_162_009]

9:	Bit 77 (MCP23S17 #5 GPB6, bank 6:bit 5)

[DAQ_HRS_162_010]

10:	Gnd

[DAQ_HRS_162_011]

11:	Bit 78 (MCP23S17 #5 GPB5, bank 6:bit 6)

[DAQ_HRS_162_012]

12:	Gnd

[DAQ_HRS_162_013]

13:	Bit 79 (MCP23S17 #5 GPB4, bank 6:bit 7)

[DAQ_HRS_162_014]

14:	Gnd

[DAQ_HRS_162_015]

15:	Bit 80 (MCP23S17 #5 GPB3, bank 6:bit 8)

[DAQ_HRS_162_016]

16:	Gnd

[DAQ_HRS_162_017]

17:	Bit 81 (MCP23S17 #5 GPB2, bank 6:bit 8)

[DAQ_HRS_162_018]

18:	Gnd

[DAQ_HRS_162_019]

19:	Bit 82 (MCP23S17 #5 GPB1, bank 6:bit 10)

[DAQ_HRS_162_020]

20:	Bit 83 (MCP23S17 #5 GPB0, bank 6:bit 11)

Note: Gnd pins are all connected to the same ground plane.

#### PPDIO96 Bank 7 Pinout

[DAQ_HRS_163_000]

The PPDIO96 Bank 7 header shall use the following pinout:

[DAQ_HRS_163_001]

1:	Bit 85 (MCP23S17 #6 GPB6, bank 7:bit 1)

[DAQ_HRS_163_002]

2:	Bit 84 (MCP23S17 #6 GPB7, bank 7:bit 0)

[DAQ_HRS_163_003]

3:	Bit 86 (MCP23S17 #6 GPB5, bank 7:bit 2)

[DAQ_HRS_163_004]

4:	Gnd

[DAQ_HRS_163_005]

5:	Bit 87 (MCP23S17 #6 GPB4, bank 7:bit 3)

[DAQ_HRS_163_006]

6:	Gnd

[DAQ_HRS_163_007]

7:	Bit 88 (MCP23S17 #6 GPB3, bank 7:bit 4)

[DAQ_HRS_163_008]

8:	Gnd

[DAQ_HRS_163_009]

9:	Bit 89 (MCP23S17 #6 GPB2, bank 7:bit 5)

[DAQ_HRS_163_010]

10:	Gnd

[DAQ_HRS_163_011]

11:	Bit 90 (MCP23S17 #6 GPB1, bank 7:bit 6)

[DAQ_HRS_163_012]

12:	Gnd

[DAQ_HRS_163_013]

13:	Bit 91 (MCP23S17 #6 GPB0, bank 7:bit 7)

[DAQ_HRS_163_014]

14:	Gnd

[DAQ_HRS_163_015]

15:	Bit 8 (MCP23S17 #6 GPA7, bank 7:bit 8)

[DAQ_HRS_163_015]

16:	Gnd

[DAQ_HRS_163_017]

17:	Bit 92 (MCP23S17 #6 GPA6, bank 7:bit 9)

[DAQ_HRS_163_018]

18:	Gnd

[DAQ_HRS_163_019]

19:	Bit 93 (MCP23S17 #6 GPA5, bank 7:bit 10)

[DAQ_HRS_163_020]

20:	Bit 94 (MCP23S17 #6 GPA4, bank 7:bit 11)

Note: Gnd pins are all connected to the same ground plane.

#### PPDIO96 DIP Switches

[DAQ_HRS_164_000]

The PPDIO96 shall provide 8 DIP switches connected to bits 88-95 (bank 7, bits 4-11).

#### PPDIO96 Power Supply Connection

[DAQ_HRS_165_000]

The PPDIO96 shall provide a two-pin screw terminal connector (5mm centers) to accept 5V/Gnd from an external power supply

#### PPDIO96 Power Supply LED

[DAQ_HRS_166_000]

The PPDIO96 shall provide an LED that is illuminated whenever power is applied to the board.

#### PPDIO96 Buffered Inputs

[DAQ_HRS_167_000]

The PPDIO96 shall provide buffering so that it presents a single TTL load to the following signals:

[DAQ_HRS_167_001]

- MOSI

[DAQ_HRS_167_002]

- SPI-CLK

[DAQ_HRS_167_003]

- RESET

#### PPDIO96 Buffered Output

[DAQ_HRS_168_000]

The PPDIO96 shall provide buffering for the MISO output line

#### PPDIO96 Tri-state Buffering

[DAQ_HRS_169_000]

The PPDIO96 buffering shall be tri-state with the buffer output lines active only when the CS/BS1 signal is active.

### 12-Channel Optoisolator Parallel Input Board (PPOPTO-12)

#### PPOPTO-12 Capacity

[DAQ_HRS_200_000]

The PPOPTO-12 shall provide 12 bits of optically-isolated digital inputs.

#### PPOPTO-12 Power Supply Connection

[DAQ_HRS_201_000]

The PPOPTO-12  board shall provide a two-pin screw terminal connector (5mm centers) to accept 5V/Gnd from an external power supply

#### PPOPTO-12 Power Supply LED

[DAQ_HRS_202_000]

The PPOPTO-12  board shall provide an LED that is illuminated whenever power is applied to the board.

#### PPOPTO-12 Output Connector Pinout

[DAQ_HRS_203_000]

The PPOPTO-12 board shall provide a 20-pin (2x10) header that is compatible with the PPDIO96 bank pinouts, using the following pinout:

[DAQ_HRS_203_001]

1:	Bit 1

[DAQ_HRS_203_002]

2:	Bit 0

[DAQ_HRS_203_003]

3:	Bit 2

[DAQ_HRS_203_004]

4:	Gnd

[DAQ_HRS_203_005]

5:	Bit 3

[DAQ_HRS_203_006]

6:	Gnd

[DAQ_HRS_203_007]

7:	Bit 4

[DAQ_HRS_203_008]

8:	Gnd

[DAQ_HRS_203_009]

9:	Bit 5

[DAQ_HRS_203_010]

10:	Gnd

[DAQ_HRS_203_011]

11:	Bit 6

[DAQ_HRS_203_012]

12:	Gnd

[DAQ_HRS_203_013]

13:	Bit 7

[DAQ_HRS_203_014]

14:	Gnd

[DAQ_HRS_203_015]

15:	Bit 8

[DAQ_HRS_203_016]

16:	Gnd

[DAQ_HRS_203_017]

17:	Bit 9

[DAQ_HRS_203_018]

18:	Gnd

[DAQ_HRS_203_019]

19:	Bit 10

[DAQ_HRS_203_020]

20:	Bit 11

Note: Gnd pins are all connected to the same ground plane.

#### PPOPTO-12 Signal LEDs

[DAQ_HRS_204_000]

The PPOPTO-12 board shall provide 12 signal LEDs.

#### PPOPTO-12 Signal LED #0 Illumination

[DAQ_HRS_205_000]

Signal LED #0 on the PPOPTO-12 board shall illuminate when input D0 is active.

[DAQ_HRS_205_001]

Signal LED #0 on the PPOPTO-12 board shall not illuminate when input D0 is inactive.

#### PPOPTO-12 Bit 0 Signal

[DAQ_HRS_205_002]

Pin #2 on the PPDIO connector shall go active when input D0 is active.

[DAQ_HRS_205_003]

Pin #2 on the PPDIO connector shall go inactive when input D0 is inactive.

#### PPOPTO-12 Signal LED #1 Illumination

[DAQ_HRS_206_000]

Signal LED #1 on the PPOPTO-12 board shall illuminate when input D1 is active.

[DAQ_HRS_206_001]

Signal LED #1 on the PPOPTO-12 board shall not illuminate when input D1 is inactive.

#### PPOPTO-12 Bit 1 Signal

[DAQ_HRS_206_002]

Pin #1 on the PPDIO connector shall go active when input D1 is active.

[DAQ_HRS_206_003]

Pin #1 on the PPDIO connector shall go inactive when input D1 is inactive.

#### PPOPTO-12 Signal LED #2 Illumination

[DAQ_HRS_207_000]

Signal LED #2 on the PPOPTO-12 board shall illuminate when input D2 is active.

[DAQ_HRS_207_001]

Signal LED #2 on the PPOPTO-12 board shall not illuminate when input D2 is inactive.

#### PPOPTO-12 Bit 2 Signal

[DAQ_HRS_207_002]

Pin #3 on the PPDIO connector shall go active when input D2 is active.

[DAQ_HRS_207_003]

Pin #3 on the PPDIO connector shall go inactive when input D2 is inactive.

#### PPOPTO-12 Signal LED #3 Illumination

[DAQ_HRS_208_000]

Signal LED #3 on the PPOPTO-12 board shall illuminate when input D3 is active.

[DAQ_HRS_208_001]

Signal LED #3 on the PPOPTO-12 board shall not illuminate when input D3 is inactive.

#### PPOPTO-12 Bit 3 Signal

[DAQ_HRS_208_002]

Pin #5 on the PPDIO connector shall go active when input D3 is active.

[DAQ_HRS_208_003]

Pin #5 on the PPDIO connector shall go inactive when input D3 is inactive.

#### PPOPTO-12 Signal LED #4 Illumination

[DAQ_HRS_209_000]

Signal LED #4 on the PPOPTO-12  board shall illuminate when input D4 is active.

[DAQ_HRS_209_001]

Signal LED #4 on the PPOPTO-12  board shall not illuminate when input D4 is inactive.

#### PPOPTO-12  Bit 4 Signal

[DAQ_HRS_209_002]

Pin #7 on the PPDIO connector shall go active when input D4 is active.

[DAQ_HRS_209_003]

Pin #7 on the PPDIO connector shall go inactive when input D4 is inactive.

#### PPOPTO-12  Signal LED #5 Illumination

[DAQ_HRS_210_000]

Signal LED #5 on the PPOPTO-12  board shall illuminate when input D5 is active.

[DAQ_HRS_210_001]

Signal LED #5 on the PPOPTO-12  board shall not illuminate when input D5 is inactive.

#### PPOPTO-12  Bit 5 Signal

[DAQ_HRS_210_002]

Pin #9 on the PPDIO connector shall go active when input D5 is active.

[DAQ_HRS_210_003]

Pin #9 on the PPDIO connector shall go inactive when input D5 is inactive.

#### PPOPTO-12  Signal LED #6 Illumination

[DAQ_HRS_211_000]

Signal LED #6 on the PPOPTO-12  board shall illuminate when input D6 is active.

[DAQ_HRS_211_001]

Signal LED #6 on the PPOPTO-12  board shall not illuminate when input D6 is inactive.

#### PPOPTO-12  Bit 6 Signal

[DAQ_HRS_211_002]

Pin #11 on the PPDIO connector shall go active when input D6 is active.

[DAQ_HRS_211_003]

Pin #11 on the PPDIO connector shall go inactive when input D6 is inactive.

#### PPOPTO-12  Signal LED #7 Illumination

[DAQ_HRS_212_000]

Signal LED #7 on the PPOPTO-12  board shall illuminate when input D7 is active.

[DAQ_HRS_212_001]

Signal LED #7 on the PPOPTO-12  board shall not illuminate when input D7 is inactive.

#### PPOPTO-12  Bit 7 Signal

[DAQ_HRS_212_002]

Pin #13 on the PPDIO connector shall go active when input D7 is active.

[DAQ_HRS_212_003]

Pin #13 on the PPDIO connector shall go inactive when input D7 is inactive.

#### PPOPTO-12  Signal LED #8 Illumination

[DAQ_HRS_213_000]

Signal LED #8 on the PPOPTO-12  board shall illuminate when input D8 is active.

[DAQ_HRS_213_001]

Signal LED #8 on the PPOPTO-12  board shall not illuminate when input D8 is inactive.

#### PPOPTO-12  Bit 8 Signal

[DAQ_HRS_213_001]

Pin #15 on the PPDIO connector shall go active when input D8 is active.

[DAQ_HRS_213_003]

Pin #15 on the PPDIO connector shall go inactive when input D8 is inactive.

#### PPOPTO-12  Signal LED #9 Illumination

[DAQ_HRS_214_000]

Signal LED #9 on the PPOPTO-12  board shall illuminate when input D9 is active.

[DAQ_HRS_214_001]

Signal LED #9 on the PPOPTO-12  board shall not illuminate when input D9 is inactive.

#### PPOPTO-12  Bit 9 Signal

[DAQ_HRS_214_002]

Pin #17 on the PPDIO connector shall go active when input D9 is active.

[DAQ_HRS_214_003]

Pin #17 on the PPDIO connector shall go inactive when input D9 is inactive.

#### PPOPTO-12  Signal LED #10 Illumination

[DAQ_HRS_215_000]

Signal LED #10 on the PPOPTO-12  board shall illuminate when input D10 is active.

[DAQ_HRS_215_001]

Signal LED #10 on the PPOPTO-12  board shall not illuminate when input D10 is inactive.

#### PPOPTO-12  Bit 10 Signal

[DAQ_HRS_215_002]

Pin #19 on the PPDIO connector shall go active when input D10 is active.

[DAQ_HRS_215_003]

Pin #19 on the PPDIO connector shall go inactive when input D10 is inactive.

#### PPOPTO-12  Signal LED #11 Illumination

[DAQ_HRS_216_000]

Signal LED #11 on the PPOPTO-12  board shall illuminate when input D11 is active.

[DAQ_HRS_216_001]

Signal LED #11 on the PPOPTO-12  board shall  not illuminate when input D11 is inactive.

#### PPOPTO-12  Bit 20 Signal

[DAQ_HRS_216_002]

Pin #20 on the PPDIO connector shall go active when input D11 is active.

[DAQ_HRS_216_003]

Pin #20 on the PPDIO connector shall go inactive when input D11 is inactive.

#### PPOPTO-12  Electrical Isolation

[DAQ_HRS_217_000]

Each input channel on the PPOPTO-12  board shall electrically isolated from the other input channels.

Note: this implies that each channel must have an isolated power supply in order to work with dry contact inputs.

#### PPOPTO-12  Dry Contact Input Selection

[DAQ_HRS_218_000]

Each input channel on the PPOPTO-12  board shall offer the ability to work with a dry contact input.

Note: Dry contact inputs require an isolated power supply for each input channel.

#### PPOPTO-12  Voltage Input Selection

[DAQ_HRS_219_000]

Each input channel on the PPOPTO-12  board shall offer the ability to accept a voltage logic-level input (supplied by the external circuitry).

#### PPOPTO-12  Voltage Input Range

[DAQ_HRS_220_000]

Each input channel on the PPOPTO-12  board shall be able to work with voltage inputs (at least) in the range 5-15V.

Note: programming the input voltage may necessitate changing a resistor.

#### PPOPTO-12  Input Connectors

[DAQ_HRS_221_000]

The PPOPTO-12  board shall provide a two-pin screw terminal for each input (5mm centers).

### 16-Channel Solid-State Relay Output Board (PPSSR16)

#### PPSSR16 Capacity

[DAQ_HRS_250_000]

The PPSSR16 board shall provide 16 output channels (bits).

#### PPSSR16 Power Supply Connection

[DAQ_HRS_251_000]

The PPSSR16 board shall provide a two-pin screw terminal connector (5mm centers) to accept 5V/Gnd from an external power supply

#### PPSSR16 Power Supply LED

[DAQ_HRS_252_000]

The PPSSR16 board shall provide an LED that is illuminated whenever power is applied to the board.

#### PPSSR16 Input Interface Connection

[DAQ_HRS_253_000]

The PPSSR16 board shall communicate with the DAQIF using the PPDO connector on the DAQIF (replicated as input connector on the PPSSR16 board); the pinout is described in [DAQ_HRS_077_000]

#### PPSSR16 Daisy Chain Connection

[DAQ_HRS_254_000]

The PPSSR16 board shall pass through the following signals from the input connector to the output connector:

[DAQ_HRS_254_001]

1:	BSO (SPI bus chip select #0)

[DAQ_HRS_254_002]

2:	No connection to input PPDO connector. Connected to Vcc (+5V) on PPSSR16 board.

[DAQ_HRS_254_003]

3:	MISO

[DAQ_HRS_254_004]

4:	– (MOSI, not passed through, see [DAQ_HRS_255_000], [DAQ_HRS_258_000], and [DAQ_HRS_259_000])

[DAQ_HRS_254_005]

5:	SPI-CLK

[DAQ_HRS_254_006]

6:	J2_38[DAQ_HRS_254_007]

7:	Reset

[DAQ_HRS_254_008]

8:	WD_LATCH

[DAQ_HRS_254_009]

9:	IRQ

[DAQ_HRS_254_010]

10:	Gnd

#### PPSSR16 Daisy Chaining

[DAQ_HRS_255_000]

The PPSSR16 board shall pass the SER OUT output of the second on-board TPIC6B595PTH  serial shift register through to the MOSI pin (pin 4) on the output PPDO connection.

#### PPSSR16 BS0 Signal

[DAQ_HRS_256_000]

The PPSSR16 board shall use the BS0 (SPI bus board/chip select #0) signal on the PPDO connector to control the transfer of the data from the internal shift register to the output latch on the TPIC6B595PTH high-current serial shift register.

Note: data is transferred from the shift register to the output latch on the rising edge of this signal – which occurs when the system completes shifting all the data out to the shift register.

#### PPSSR16 MISO Signal

[DAQ_HRS_257_000]

The PPSSR16 board shall ignore the MISO (master data in, slave out) signal on the PPDO input connector.

#### PPSSR16 MOSI Signal

[DAQ_HRS_258_000]

The PPSSR16 board shall connect the MOSI (SPI master out, slave in) input signal to the serial in pin of the first TPIC6B595PTH serial shift register.

#### PPSSR16 TPIC6B595PTH Daisy-Chaining

[DAQ_HRS_259_000]

The PPSSR16 board shall connect the SER OUT signal of the first TPIC6B595PTH IC to the SER IN signal of the second TPIC6B595PTH IC.

#### PPSSR16 TPIC6B595PTH Power-on Reset

[DAQ_HRS_260_000]

The PPSSR16 board shall clear the TPIC6B595PTH serial shift register on power up.

#### PPSSR16 TPIC6B595PTH Programmed Reset

[DAQ_HRS_261_000]

The PPSSR16 board shall clear the TPIC6B595PTH serial shift registers whenever the reset signal on the PPDO connection is asserted (active low).

Note: The reset signal on the PPDO connector is shared amongst many functions, including watchdog latch reset and MCP23S17 (on the PPDIO96) reset.

#### PPSSR16 TPIC6B595PTH Watchdog Reset

[DAQ_HRS_262_000]

The PPSSR16 board shall clear the TPIC6B595PTH serial shift registers whenever the WS Latch signal on the PPDO connection is asserted (active low).

#### PPSSR16 Data Clock

[DAQ_HRS_263_000]

The PPSSR16 board shall connect the SPI-CLK signal on the PPDO connector to the SRCK (shift register clock) on both the TPIC6B595PTH  ICs.

Note: because the two TPIC6B595PTH  ICs are connected in serials (via the SER OUT and SER In pins), it will take 16 clock pulses to shift it 16 bits of data.

#### PPSSR16 Data Output LEDs

[DAQ_HRS_264_000]

The PPSSR16 board shall provide one LED for each output channel.

#### PPSSR16 Data Output LED Illumination

[DAQ_HRS_265_000]

The PPSSR16 board shall turn on a channel's output LED when that output channel is programmed with a '1' bit.

[DAQ_HRS_265_001]

Shifting a '1' bit into the D0 bit position will illuminate the D0 LED.
Note: the D0 bit position is not necessarily bit position 0 in the serial data stream.

[DAQ_HRS_265_002]

Shifting a '0' bit into the D0 bit position will extinguish the D0 LED.
Note: the D0 bit position is not necessarily bit position 0 in the serial data stream.

[DAQ_HRS_265_003]

Shifting a '1' bit into the D1 bit position will illuminate the D1 LED.
Note: the D1 bit position is not necessarily bit position 1 in the serial data stream.

[DAQ_HRS_265_004]

Shifting a '0' bit into the D1 bit position will extinguish the D1 LED.
Note: the D1 bit position is not necessarily bit position 1 in the serial data stream.

[DAQ_HRS_265_005]

Shifting a '1' bit into the D1 bit position will illuminate the D2 LED.
Note: the D2 bit position is not necessarily bit position 2 in the serial data stream.

[DAQ_HRS_265_006]

Shifting a '0' bit into the D2 bit position will extinguish the D2 LED.
Note: the D2 bit position is not necessarily bit position 2 in the serial data stream.

[DAQ_HRS_265_007]

Shifting a '1' bit into the D3 bit position will illuminate the D3 LED.
Note: the D3 bit position is not necessarily bit position 3 in the serial data stream.

[DAQ_HRS_265_008]

Shifting a '0' bit into the D3 bit position will extinguish the D3 LED.
Note: the D3 bit position is not necessarily bit position 3 in the serial data stream.

[DAQ_HRS_265_009]

Shifting a '1' bit into the D4 bit position will illuminate the D4 LED.
Note: the D4 bit position is not necessarily bit position 4 in the serial data stream.

[DAQ_HRS_265_010]

Shifting a '0' bit into the D4 bit position will extinguish the D4 LED.
Note: the D4 bit position is not necessarily bit position 4 in the serial data stream.

[DAQ_HRS_265_011]

Shifting a '1' bit into the D5 bit position will illuminate the D5 LED.
Note: the D5 bit position is not necessarily bit position 5 in the serial data stream.

[DAQ_HRS_265_012]

Shifting a '0' bit into the D5 bit position will extinguish the D5 LED.
Note: the D5 bit position is not necessarily bit position 5 in the serial data stream.

[DAQ_HRS_265_013]

Shifting a '1' bit into the D6 bit position will illuminate the D6 LED.
Note: the D6 bit position is not necessarily bit position 6 in the serial data stream.

[DAQ_HRS_265_014]

Shifting a '0' bit into the D6 bit position will extinguish the D6 LED.
Note: the D6 bit position is not necessarily bit position 6 in the serial data stream.

[DAQ_HRS_265_015]

Shifting a '1' bit into the D7 bit position will illuminate the D7 LED.
Note: the D7 bit position is not necessarily bit position 7 in the serial data stream.

[DAQ_HRS_265_016]

Shifting a '0' bit into the D7 bit position will extinguish the D7 LED.
Note: the D7 bit position is not necessarily bit position 7 in the serial data stream.

[DAQ_HRS_265_017]

Shifting a '1' bit into the D8 bit position will illuminate the D8 LED.
Note: the D8 bit position is not necessarily bit position 8 in the serial data stream.

[DAQ_HRS_265_018]

Shifting a '0' bit into the D8 bit position will extinguish the D8 LED.
Note: the D8 bit position is not necessarily bit position 8 in the serial data stream.

[DAQ_HRS_265_019]

Shifting a '1' bit into the D9 bit position will illuminate the D9 LED.
Note: the D9 bit position is not necessarily bit position 9 in the serial data stream.

[DAQ_HRS_265_020]

Shifting a '0' bit into the D9 bit position will extinguish the D9 LED.
Note: the D9 bit position is not necessarily bit position 9 in the serial data stream.

[DAQ_HRS_265_021]

Shifting a '1' bit into the D0 bit position will illuminate the D10 LED.
Note: the D10 bit position is not necessarily bit position 10 in the serial data stream.

[DAQ_HRS_265_022]

Shifting a '0' bit into the D10 bit position will extinguish the D10 LED.
Note: the D10 bit position is not necessarily bit position 10 in the serial data stream.

[DAQ_HRS_265_023]

Shifting a '1' bit into the D11 bit position will illuminate the D11 LED.
Note: the D11 bit position is not necessarily bit position 11 in the serial data stream.

[DAQ_HRS_265_024]

Shifting a '0' bit into the D11 bit position will extinguish the D11 LED.
Note: the D11 bit position is not necessarily bit position 11 in the serial data stream.

[DAQ_HRS_265_025]

Shifting a '1' bit into the D12 bit position will illuminate the D12 LED.
Note: the D12 bit position is not necessarily bit position 12 in the serial data stream.

[DAQ_HRS_265_026]

Shifting a '0' bit into the D12 bit position will extinguish the D12 LED.
Note: the D12 bit position is not necessarily bit position 12 in the serial data stream.

[DAQ_HRS_265_027]

Shifting a '1' bit into the D13 bit position will illuminate the D13 LED.
Note: the D13 bit position is not necessarily bit position 13 in the serial data stream.

[DAQ_HRS_265_028]

Shifting a '0' bit into the D13 bit position will extinguish the D13 LED.
Note: the D13 bit position is not necessarily bit position 13 in the serial data stream.

[DAQ_HRS_265_029]

Shifting a '1' bit into the D14 bit position will illuminate the D14 LED.
Note: the D14 bit position is not necessarily bit position 14 in the serial data stream.

[DAQ_HRS_265_030]

Shifting a '0' bit into the D14 bit position will extinguish the D14 LED.
Note: the D14 bit position is not necessarily bit position 14 in the serial data stream.

[DAQ_HRS_265_031]

Shifting a '1' bit into the D15 bit position will illuminate the D15 LED.
Note: the D15 bit position is not necessarily bit position 15 in the serial data stream.

[DAQ_HRS_265_032

Shifting a '0' bit into the D15 bit position will extinguish the D15 LED.
Note: the D15 bit position is not necessarily bit position 15 in the serial data stream.

[DAQ_HRS_265_033]

Shifting a '1' bit into the D0 bit position will put the D0 SSR contacts into a low-impedance state (closed contacts).

Note: the D0 bit position is not necessarily bit position 0 in the serial data stream.

[DAQ_HRS_265_034]

Shifting a '0' bit into the D0 bit position will put the D0 SSR contacts into a high-impedance state (open contacts).

Note: the D0 bit position is not necessarily bit position 0 in the serial data stream.

[DAQ_HRS_265_035]

Shifting a '1' bit into the D1 bit position will put the D1 SSR contacts into a low-impedance state (closed contacts).

Note: the D1 bit position is not necessarily bit position 1 in the serial data stream.

[DAQ_HRS_265_036]

Shifting a '0' bit into the D1 bit position will put the D1 SSR contacts into a high-impedance state (open contacts).

Note: the D1 bit position is not necessarily bit position 1 in the serial data stream.

[DAQ_HRS_265_037]

Shifting a '1' bit into the D2 bit position will put the D2 SSR contacts into a low-impedance state (closed contacts).

Note: the D2 bit position is not necessarily bit position 2 in the serial data stream.

[DAQ_HRS_265_038]

Shifting a '0' bit into the D2 bit position will put the D2 SSR contacts into a high-impedance state (open contacts).

Note: the D2 bit position is not necessarily bit position 2 in the serial data stream.

[DAQ_HRS_265_039]

Shifting a '1' bit into the D3 bit position will put the D3 SSR contacts into a low-impedance state (closed contacts).

Note: the D3 bit position is not necessarily bit position 3 in the serial data stream.

[DAQ_HRS_265_040]

Shifting a '0' bit into the D2 bit position will put the D2 SSR contacts into a high-impedance state (open contacts).

Note: the D2 bit position is not necessarily bit position 2 in the serial data stream.

[DAQ_HRS_265_041]

Shifting a '1' bit into the D4 bit position will put the D4 SSR contacts into a low-impedance state (closed contacts).

Note: the D4 bit position is not necessarily bit position 4 in the serial data stream.

[DAQ_HRS_265_042]

Shifting a '0' bit into the D4 bit position will put the D4 SSR contacts into a high-impedance state (open contacts).

Note: the D4 bit position is not necessarily bit position 4 in the serial data stream.

[DAQ_HRS_265_043]

Shifting a '1' bit into the D5 bit position will put the D5 SSR contacts into a low-impedance state (closed contacts).

Note: the D5 bit position is not necessarily bit position 5 in the serial data stream.

[DAQ_HRS_265_044]

Shifting a '0' bit into the D5 bit position will put the D5 SSR contacts into a high-impedance state (open contacts).

Note: the D5 bit position is not necessarily bit position 5 in the serial data stream.

[DAQ_HRS_265_045]

Shifting a '1' bit into the D6 bit position will put the D6 SSR contacts into a low-impedance state (closed contacts).

Note: the D6 bit position is not necessarily bit position 6 in the serial data stream.

[DAQ_HRS_265_046]

Shifting a '0' bit into the D6 bit position will put the D6 SSR contacts into a high-impedance state (open contacts).

Note: the D6 bit position is not necessarily bit position 6 in the serial data stream.

[DAQ_HRS_265_047]

Shifting a '1' bit into the D7 bit position will put the D7 SSR contacts into a low-impedance state (closed contacts).

Note: the D7 bit position is not necessarily bit position 7 in the serial data stream.

[DAQ_HRS_265_048]

Shifting a '0' bit into the D7 bit position will put the D7 SSR contacts into a high-impedance state (open contacts).

Note: the D7 bit position is not necessarily bit position 7 in the serial data stream.

[DAQ_HRS_265_049 ]

Shifting a '1' bit into the D8 bit position will put the D8 SSR contacts into a low-impedance state (closed contacts).

Note: the D8 bit position is not necessarily bit position 8 in the serial data stream.

[DAQ_HRS_265_050]

Shifting a '0' bit into the D8 bit position will put the D8 SSR contacts into a high-impedance state (open contacts).

Note: the D8 bit position is not necessarily bit position 8 in the serial data stream.

[DAQ_HRS_265_051]

Shifting a '1' bit into the D9 bit position will put the D9 SSR contacts into a low-impedance state (closed contacts).

Note: the D9 bit position is not necessarily bit position 9 in the serial data stream.

[DAQ_HRS_265_052]

Shifting a '0' bit into the D9 bit position will put the D9 SSR contacts into a high-impedance state (open contacts).

Note: the D9 bit position is not necessarily bit position 9 in the serial data stream.

[DAQ_HRS_265_053]

Shifting a '1' bit into the D10 bit position will put the D10 SSR contacts into a low-impedance state (closed contacts).

Note: the D10 bit position is not necessarily bit position 10 in the serial data stream.

[DAQ_HRS_265_054]

Shifting a '0' bit into the D10 bit position will put the D10 SSR contacts into a high-impedance state (open contacts).

Note: the D10 bit position is not necessarily bit position 10 in the serial data stream.

[DAQ_HRS_265_055]

Shifting a '1' bit into the D11 bit position will put the D11 SSR contacts into a low-impedance state (closed contacts).

Note: the D11 bit position is not necessarily bit position 11 in the serial data stream.

[DAQ_HRS_265_056]

Shifting a '0' bit into the D11 bit position will put the D11 SSR contacts into a high-impedance state (open contacts).

Note: the D11 bit position is not necessarily bit position 11 in the serial data stream.

[DAQ_HRS_265_057]

Shifting a '1' bit into the D12 bit position will put the D12 SSR contacts into a low-impedance state (closed contacts).

Note: the D12 bit position is not necessarily bit position 12 in the serial data stream.

[DAQ_HRS_265_058]

Shifting a '0' bit into the D12 bit position will put the D12 SSR contacts into a high-impedance state (open contacts).

Note: the D12 bit position is not necessarily bit position 12 in the serial data stream.

[DAQ_HRS_265_059]

Shifting a '1' bit into the D13 bit position will put the D13 SSR contacts into a low-impedance state (closed contacts).

Note: the D13 bit position is not necessarily bit position 13 in the serial data stream.

[DAQ_HRS_265_060]

Shifting a '0' bit into the D13 bit position will put the D13 SSR contacts into a high-impedance state (open contacts).

Note: the D13 bit position is not necessarily bit position 13 in the serial data stream.

[DAQ_HRS_265_061]

Shifting a '1' bit into the D14 bit position will put the D14 SSR contacts into a low-impedance state (closed contacts).

Note: the D14 bit position is not necessarily bit position 14 in the serial data stream.

[DAQ_HRS_265_062]

Shifting a '0' bit into the D14 bit position will put the D14 SSR contacts into a high-impedance state (open contacts).

Note: the D14 bit position is not necessarily bit position 14 in the serial data stream.

[DAQ_HRS_265_063]

Shifting a '1' bit into the D15 bit position will put the D15 SSR contacts into a low-impedance state (closed contacts).

Note: the D15 bit position is not necessarily bit position 15 in the serial data stream.

[DAQ_HRS_265_064]

Shifting a '0' bit into the D1 bit position will put the D1 SSR contacts into a high-impedance state (open contacts).

Note: the D15 bit position is not necessarily bit position 15 in the serial data stream.

#### PPSSR16 Output Isolation

[DAQ_HRS_266_000]

The PPSSR16 board shall provide isolation for all outputs.

#### PPSSR16 Output Current Capacity

[DAQ_HRS_267_000]

The PPSSR16 board shall have relays capable of handling 2A.

Note: this does not imply that each channel on the PPSSR16 board can handle 2 amps. The usual engineering derating (by ½ to 1A) as well as concerns about temperature increases on traces need to be considered when choosing the actual maximum current possible on each SSR.

#### PPSSR16 Output Voltage Capacity

[DAQ_HRS_268_000]

The PPSSR16 board shall be capable of handling 30VDC on each output channel.

#### PPSSR16 Output Connectors

[DAQ_HRS_269_000]

The PPSSR16 board shall provide a two-pin screw terminal for each relay output (5mm centers).

#### PPSSR16 Relay Sockets

[DAQ_HRS_270_000]

The PPSSR16 board shall provide sockets for each solid-state relay on the board.]

(Deprecated)

#### PPSSR16 Buffered SPI Clock signal

[DAQ_HRS_271_000]

The PPSSR16 board shall buffer the incoming SPI-CLK (SCK) signal so that the board presents only one TTL load for this signal.

#### PPSSR16 Buffered RESET signal

[DAQ_HRS_272_000]

The PPSSR16 board shall buffer the incoming RESET signal so that the board presents only one TTL load for this signal.

#### PPSSR16 Buffered Watchdog Latch signal

[DAQ_HRS_273_000]

The PPSSR16 board shall buffer the incoming Watchdog Latch (WD_Latch) signal so that the board presents only one TTL load for this signal.

### 12-Channel Mechanical Relay Output Board (PPRELAY12)

#### PPRELAY12 Capacity

[DAQ_HRS_300_000]

The PPRELAY12  board shall provide 12 output channels (bits).

#### PPRELAY12 Power Supply Connection

[DAQ_HRS_301_000]

The PPRELAY12 board shall provide a two-pin screw terminal connector (5mm centers) to accept 5V/Gnd from an external power supply

#### PPRELAY12 Power Supply LED

[DAQ_HRS_302_000]

The PPRELAY12 board shall provide an LED that is illuminated whenever power is applied to the board.

#### PPRELAY12 Input Interface Connection

[DAQ_HRS_303_000]

The PPRELAY12 board shall communicate with the DAQIF using the PPDO connector on the DAQIF (replicated as input connector on the PPRELAY12 board); the pinout is described in [DAQ_HRS_077_000]

#### PPRELAY12 Daisy Chain Connection

[DAQ_HRS_304_000]

The PPRELAY12 board shall pass through the following signals from the input connector to the output connector:

[DAQ_HRS_304_001]

1:	BSO (SPI bus chip select #0)

[DAQ_HRS_304_002]

2:	NC

[DAQ_HRS_304_003]

3:	MISO

[DAQ_HRS_304_004]

4:	– (MOSI, not passed through, see [DAQ_HRS_305_000], [DAQ_HRS_308_000], and [DAQ_HRS_309_000])

[DAQ_HRS_304_005]

5:	SPI-CLK

[DAQ_HRS_304_006]

6:	J2_38

[DAQ_HRS_304_007]

7:	Reset

[DAQ_HRS_304_008]

8:	WD_LATCH

[DAQ_HRS_304_009]

9:	IRQ

[DAQ_HRS_304_010]

10:	Gnd

#### PPRELAY12 Daisy Chaining

[DAQ_HRS_305_000]

The PPRELAY12 board shall pass the SER OUT output of the second on-board TPIC6B595PTH  serial shift register through to the MOSI pin (pin 4) on the output PPDO connection.

#### PPRELAY12 BS0 Signal

[DAQ_HRS_306_000]

The PPRELAY12 board shall use the BS0 (SPI bus board/chip select #0) signal on the PPDO connector to control the transfer of the data from the internal shift register to the output latch on the TPIC6B595PTH high-current serial shift register.

Note: data is transferred from the shift register to the output latch on the rising edge of this signal – which occurs when the system completes shifting all the data out to the shift register.

#### PPRELAY12 MISO Signal

[DAQ_HRS_307_000]

The PPRELAY12 board shall ignore the MISO (master data in, slave out) signal on the PPDO connector.

#### PPRELAY12 MOSI Signal

[DAQ_HRS_308_000]

The PPRELAY12 board shall connect the MOSI (SPI master out, slave in) input signal to the serial in pin of the first TPIC6B595PTH serial shift register.

#### PPRELAY12 TPIC6B595PTH Daisy-Chaining

[DAQ_HRS_309_000]

The PPRELAY12 board shall connect the SER OUT signal of the first TPIC6B595PTH IC to the SER IN signal of the second TPIC6B595PTH IC.

#### PPRELAY12 TPIC6B595PTH Power-on Reset

[DAQ_HRS_310_000]

The PPRELAY12 board shall clear the TPIC6B595PTH serial shift register on power up.

#### PPRELAY12 TPIC6B595PTH Programmed Reset

[DAQ_HRS_311_000]

The PPRELAY12 board shall clear the TPIC6B595PTH serial shift register whenever the reset signal on the PPDO connection is asserted (active low).

Note: The reset signal on the PPDO connector is shared amongst many functions, including watchdog latch reset and MCP23S17 (on the PPDIO96) reset.

#### PPRELAY12 Watchdog Latch Reset

[DAQ_HRS_312_000]

The PPRELAY12 board shall clear the TPIC6B595PTH serial shift register whenever the WD Latch signal on the PPDO connection is asserted (active low).

#### PPRELAY12 Data Clock

[DAQ_HRS_313_000]

The PPRELAY12 board shall connect the SPI-CLK signal on the PPDO connector to the SRCK (shift register clock) on both the TPIC6B595PTH  ICs.

Note: because the two TPIC6B595PTH  ICs are connected in serials (via the SER OUT and SER In pins), it will take 16 clock pulses to shift in 16 bits of data.

#### PPRELAY12 Data Output LEDs

[DAQ_HRS_314_000]

The PPRELAY12 board shall provide one LED for each output channel.

#### PPRELAY12 Data Output LED Illumination

[DAQ_HRS_315_000]

The PPRELAY12 board shall turn on a channel's output LED when that output channel is programmed with a '1' bit.

[DAQ_HRS_315_001]

Shifting a '1' bit into the D0 bit position will illuminate the D0 LED.

Note: the D0 bit position isn't necessarily the bit in position 0 of the serial output stream.

[DAQ_HRS_315_002]

Shifting a '0' bit into the D0 bit position will extinguish the D0 LED.

Note: the D0 bit position isn't necessarily the bit in position 0 of the serial output stream.

[DAQ_HRS_315_003]

Shifting a '1' bit into the D1 bit position will illuminate the D1 LED.

Note: the D1 bit position isn't necessarily the bit in position 1 of the serial output stream.

[DAQ_HRS_315_004]

Shifting a '0' bit into the D1 bit position will extinguish the D1 LED.

Note: the D1 bit position isn't necessarily the bit in position 1 of the serial output stream.

[DAQ_HRS_315_005]

Shifting a '1' bit into the D2 bit position will illuminate the D2 LED.

Note: the D2 bit position isn't necessarily the bit in position 2 of the serial output stream.

[DAQ_HRS_315_006]

Shifting a '0' bit into the D2 bit position will extinguish the D2 LED.

Note: the D2 bit position isn't necessarily the bit in position 2 of the serial output stream.

[DAQ_HRS_315_007]

Shifting a '1' bit into the D3 bit position will illuminate the D3 LED.

Note: the D3 bit position isn't necessarily the bit in position 3 of the serial output stream.

[DAQ_HRS_315_008]

Shifting a '0' bit into the D3 bit position will extinguish the D3 LED.

Note: the D3 bit position isn't necessarily the bit in position 3 of the serial output stream.

[DAQ_HRS_315_009]

Shifting a '1' bit into the D4 bit position will illuminate the D4 LED.

Note: the D4 bit position isn't necessarily the bit in position 4 of the serial output stream.

[DAQ_HRS_315_010]

Shifting a '0' bit into the D4 bit position will extinguish the D4 LED.

Note: the D4 bit position isn't necessarily the bit in position 4 of the serial output stream.

[DAQ_HRS_315_011]

Shifting a '1' bit into the D5 bit position will illuminate the D5 LED.

Note: the D5 bit position isn't necessarily the bit in position 5 of the serial output stream.

[DAQ_HRS_315_012]

Shifting a '0' bit into the D5 bit position will extinguish the D5 LED.

Note: the D5 bit position isn't necessarily the bit in position 5 of the serial output stream.

[DAQ_HRS_315_013]

Shifting a '1' bit into the D6 bit position will illuminate the D6 LED.

Note: the D6 bit position isn't necessarily the bit in position 6 of the serial output stream.

[DAQ_HRS_315_014]

Shifting a '0' bit into the D6 bit position will extinguish the D6 LED.

Note: the D6 bit position isn't necessarily the bit in position 6 of the serial output stream.

[DAQ_HRS_315_015]

Shifting a '1' bit into the D7 bit position will illuminate the D7 LED.

Note: the D7 bit position isn't necessarily the bit in position 7 of the serial output stream.

[DAQ_HRS_315_016]

Shifting a '0' bit into the D7 bit position will extinguish the D7 LED.

Note: the D7 bit position isn't necessarily the bit in position 7 of the serial output stream.

[DAQ_HRS_315_017]

Shifting a '1' bit into the D8 bit position will illuminate the D8 LED.

Note: the D8 bit position isn't necessarily the bit in position 8 of the serial output stream.

[DAQ_HRS_315_018]

Shifting a '0' bit into the D8 bit position will extinguish the D8 LED.

Note: the D8 bit position isn't necessarily the bit in position 8 of the serial output stream.

[DAQ_HRS_315_019]

Shifting a '1' bit into the D9 bit position will illuminate the D9 LED.

Note: the D9 bit position isn't necessarily the bit in position 9 of the serial output stream.

[DAQ_HRS_315_020]

Shifting a '0' bit into the D9 bit position will extinguish the D9 LED.

Note: the D9 bit position isn't necessarily the bit in position 9 of the serial output stream.

[DAQ_HRS_315_021]

Shifting a '1' bit into the D10 bit position will illuminate the D10 LED.

Note: the D10 bit position isn't necessarily the bit in position 10 of the serial output stream.

[DAQ_HRS_315_022]

Shifting a '0' bit into the D10 bit position will extinguish the D10 LED.

Note: the D10 bit position isn't necessarily the bit in position 10 of the serial output stream.

[DAQ_HRS_315_023]

Shifting a '1' bit into the D11 bit position will illuminate the D11 LED.

Note: the D11 bit position isn't necessarily the bit in position 11 of the serial output stream.

[DAQ_HRS_315_024]

Shifting a '0' bit into the D11 bit position will extinguish the D11 LED.

Note: the D11 bit position isn't necessarily the bit in position 11 of the serial output stream.

#### PPRELAY12 Auxiliary Output Bits Connector

[DAQ_HRS_316_000]

The PPRELAY12 board shall route the extra 4 bits (TPIC6B595PTH  ICs produce 16 output bits, there are only 12 relays) to an 8-pin connector (2x4) with the following pinout:

[DAQ_HRS_316_001]

1:	Bit 12 output

[DAQ_HRS_316_002]

2:	Vcc (5V)

[DAQ_HRS_316_003]

3:	Bit 13 output

[DAQ_HRS_316_004]

4:	Vcc (5V)

[DAQ_HRS_316_005]

5:	Bit 14 output

[DAQ_HRS_316_006]

6:	Vcc (5V)

[DAQ_HRS_316_007]

7:	Bit 15 output

[DAQ_HRS_316_008]

8:	Vcc (5V)

Note: the TPIC6B595PTH  IC provides open-drain outputs and pulls the signal to ground when active. This is why the alternate pins have +5V applied rather than ground (the TPIC6B595PTH  pins serve as the ground).

#### PPRELAY12 Output Isolation

[DAQ_HRS_317_000]

The PPSSR16 board shall provide isolation for all outputs.

Note: this feature is provided by default given the nature of mechanical relays.

#### PPRELAY12 Output Current Capacity

[DAQ_HRS_318_000]

The PPRELAY12 board shall be capable of handling 2A on each output channel.

Note: typical relays specified for the PPRELAY-12 board handle 5A. However, this does not imply that the board can handle 5A. First of all, you always derate by ½ (that is, 2.5A). Furthermore, with 100 mil traces you get a 10 C temperature rise on 100 mil traces at 2A. Therefore, 2A is probably the maximum you would want to realistically feed through the traces (even with 2 oz copper boards).

#### PPRELAY12 Output Voltage Capacity

[DAQ_HRS_319_000]

The PPRELAY12 board shall be capable of handling a minimum of  30VDC on each output channel.

#### PPRELAY12 Output Connectors

[DAQ_HRS_320_000]

The PPRELAY12 board shall provide a three-pin screw terminal for each relay output (5mm centers) for NC/COMM/NO relay connections.

#### PPRELAY12 NC Optional

[DAQ_HRS_321_000]

The PPRELAY12 board shall provide the option of using SPST relays (with NO/COM connections only) by swapping relays and substituting two-terminal connections in place of the three-terminal connections ([DAQ_HRS_320_000]).

#### PPRELAY12 Buffered SPI Clock signal

[DAQ_HRS_322_000]

The PPRELAY12 board shall buffer the incoming SPI-CLK (SCK) signal so that the board presents only one TTL load for this signal.

#### PPRELAY12 Buffered RESET signal

[DAQ_HRS_323_000]

The PPRELAY12 board shall buffer the incoming RESET signal so that the board presents only one TTL load for this signal.

#### PPRELAY12 Buffered Watchdog Latch signal

[DAQ_HRS_324_000]

The PPRELAY12 board shall buffer the incoming Watchdog Latch (WD_Latch) signal so that the board presents only one TTL load for this signal.

#### PPRELAY12 Buffered BS0 signal

[DAQ_HRS_325_000]

The PPRELAY12 board shall buffer the incoming BS0 signal so that the board presents only one TTL load for this signal.

### 48-Channel Digital Output Board (PPDO-48)

#### PPDO-48 Capacity

[DAQ_HRS_330_000]

The PPDO-48 board shall provide 48 output channels (bits).

#### PPDO-48 Power Supply Connection

[DAQ_HRS_341_000]

The PPDO-48 board shall provide a two-pin screw terminal connector (5mm centers) to accept 5V/Gnd from an external power supply

#### PPDO-48 Power Supply LED

[DAQ_HRS_332_000]

The PPDO-48 board shall provide an LED that is illuminated whenever power is applied to the board.

#### PPDO-48 Input Interface Connection

[DAQ_HRS_333_000]

The PPDO-48 board shall communicate with the DAQIF using the PPDO connector on the DAQIF (replicated as input connector on the PPDO48 board); the pinout is described in [DAQ_HRS_077_000]

#### PPDO-48 Daisy Chain Connection

[DAQ_HRS_334_000]

The PPDO-48 board shall pass through the following signals from the input connector to the output connector:

[DAQ_HRS_334_001]

1:	BSO (SPI bus chip select #0)

[DAQ_HRS_334_002]

2:	NC

[DAQ_HRS_334_003]

3:	MISO

[DAQ_HRS_334_004]

4:	– (MOSI, not passed through, [DAQ_HRS_335_000], [DAQ_HRS_338_000] and [DAQ_HRS_339_000])

[DAQ_HRS_334_005]

5:	SPI-CLK

[DAQ_HRS_334_006]

6:	J2_38

[DAQ_HRS_334_007]

7:	Reset

[DAQ_HRS_334_008]

8:	WD_LATCH

[DAQ_HRS_334_009]

9:	IRQ

[DAQ_HRS_334_010]

10:	Gnd

#### PPDO48 Daisy Chaining

[DAQ_HRS_335_000]

The PPDO-48 board shall pass the SER OUT output of the last on-board TPIC6B595  serial shift register through to the MOSI pin (pin 4) on the output PPDO connection.

#### PPDO-48 BS0 Signal

[DAQ_HRS_336_000]

The PPDO-48 board shall use the BS0 (SPI bus board/chip select #0) signal on the PPDO connector to control the transfer of the data from the internal shift register to the output latch on the TPIC6B595 high-current serial shift registers.

Note: data is transferred from the shift register to the output latch on the rising edge of this signal – which occurs when the system completes shifting all the data out to the shift register.

#### PPDO-48 MISO Signal

[DAQ_HRS_337_000]

The PPDO-48 board shall ignore the MISO (master data in, slave out) signal on the PPDO connector.

#### PPDO-48 MOSI Signal

[DAQ_HRS_338_000]

The PPDO-48 board shall connect the MOSI (SPI master out, slave in) input signal to the serial in pin of the first TPIC6B595 serial shift register.

#### PPDO48 TPIC6B595 Daisy-Chaining #1

[DAQ_HRS_339_000]

The PPDO-48 board shall connect the SER OUT signal of the first TPIC6B595 IC to the SER IN signal of the second TPIC6B595 IC.

[DAQ_HRS_339.1_000]

The PPDO-48 board shall connect the SER OUT signal of the second TPIC6B595PTH IC to the SER IN signal of the third TPIC6B595PTH IC.

[DAQ_HRS_339.2_000]

The PPDO-48 board shall connect the SER OUT signal of the third TPIC6B595PTH IC to the SER IN signal of the fourth TPIC6B595PTH IC.

[DAQ_HRS_339.3_000]

The PPDO-48 board shall connect the SER OUT signal of the fourth TPIC6B595PTH IC to the SER IN signal of the fifth TPIC6B595PTH IC.

[DAQ_HRS_339.4_000]

The PPDO-48 board shall connect the SER OUT signal of the fifth TPIC6B595PTH IC to the SER IN signal of the sixth (last) TPIC6B595PTH IC.

#### PPDO-48 TPIC6B595 Power-on Reset

[DAQ_HRS_340_000]

The PPDO-48 board shall clear the TPIC6B595 serial shift registers on power up.

#### PPDO-48 TPIC6B595 Programmed Reset

[DAQ_HRS_341_000]

The PPDO-48 board shall clear the TPIC6B595 serial shift registers whenever the reset signal on the PPDO connection is asserted (active low).

Note: The reset signal on the PPDO connector is shared amongst many functions, including watchdog latch reset and MCP23S17 (on the PPDIO96) reset.

#### PPDO-48 Watchdog Latch Reset

[DAQ_HRS_342_000]

The PPDO-48 board shall clear the TPIC6B595 serial shift register whenever the WD Latch signal on the PPDO connection is asserted (active low).

#### PPDO-48 Data Clock

[DAQ_HRS_343_000]

The PPDO-48 board shall connect the SPI-CLK signal on the PPDO connector to the SRCK (shift register clock) on both the TPIC6B595  ICs.

Note: because the six TPIC6B595  ICs are connected in series (via the SER OUT and SER In pins), it will take 48 clock pulses to shift in 48 bits of data.

#### PPDO-48 Output Connectors

[DAQ_HRS_344.001_000]

The PPDO-48 board shall support six 16-pin output connectors (one for each TPIC6B595 IC on the board).

#### PPDO-48 Output Connector (Bank 0)

[DAQ_HRS_344.002_000]

The first data output connector on the PPDO-48 shall support the following pinout:

- Vcc

- D0

- Vcc

- D1

- Vcc

- D2

- Vcc

- D3

- Gnd

- D4

- Gnd

- D5

- Gnd

- D6

- Gnd

- D7

#### PPDO-48 Output Connector (Bank 1)

[DAQ_HRS_344.003_000]

The second data output connector on the PPDO-48 shall support the following pinout:

- Vcc

- D8

- Vcc

- D9

- Vcc

- D10

- Vcc

- D11

- Gnd

- D12

- Gnd

- D13

- Gnd

- D14

- Gnd

- D15

#### PPDO-48 Output Connector (Bank 2)

[DAQ_HRS_344.004_000]

The third data output connector on the PPDO-48 shall support the following pinout:

- Vcc

- D16

- Vcc

- D17

- Vcc

- D18

- Vcc

- D19

- Gnd

- D20

- Gnd

- D21

- Gnd

- D22

- Gnd

- D23

#### PPDO-48 Output Connector (Bank 3)

[DAQ_HRS_344.005_000]

The fourth data output connector on the PPDO-48 shall support the following pinout:

- Vcc

- D24

- Vcc

- D25

- Vcc

- D26

- Vcc

- D27

- Gnd

- D28

- Gnd

- D29

- Gnd

- D30

- Gnd

- D31

#### PPDO-48 Output Connector (Bank 4)

[DAQ_HRS_344.006_000]

The fifth data output connector on the PPDO-48 shall support the following pinout:

- Vcc

- D32

- Vcc

- D33

- Vcc

- D34

- Vcc

- D35

- Gnd

- D36

- Gnd

- D37

- Gnd

- D38

- Gnd

- D39

#### PPDO-48 Output Connector (Bank 5)

[DAQ_HRS_344.007_000]

The sixth data output connector on the PPDO-48 shall support the following pinout:

- Vcc

- D40

- Vcc

- D41

- Vcc

- D42

- Vcc

- D43

- Gnd

- D44

- Gnd

- D45

- Gnd

- D46

- Gnd

- D47

#### PPDO-48 Buffered SPI Clock signal

[DAQ_HRS_344.008_000]

The PPDO-48 board shall buffer the incoming SPI-CLK (SCK) signal so that the board presents only one TTL load for this signal.

#### PPDO-48 Buffered RESET signal

[DAQ_HRS_344.009_000]

The PPDO-48 board shall buffer the incoming RESET signal so that the board presents only one TTL load for this signal.

#### PPDO-48 Buffered Watchdog Latch signal

[DAQ_HRS_344.010_000]

The PPDO-48 board shall buffer the incoming WD_Latch signal so that the board presents only one TTL load for this signal.

#### PPDO-48 Buffered BS0 signal

[DAQ_HRS_344.009_011]

The PPDO-48 board shall buffer the incoming BS0 signal so that the board presents only one TTL load for this signal.

### 8-Channel Analog Input/4-Channel Analog Output Board (PPAIO-16/4)

#### PPAIO-16/4 Analog Input Capacity

[DAQ_HRS_350_000]

The PPAIO-16/4 board shall provide 16 singled-ended analog input channels.

#### PPAIO-16/4 Double-Ended Input Capacity

[DAQ_HRS_351_000]

The PPAIO-16/4 board shall allow adjacent even-odd pairs of single-ended analog inputs to be combined into a double-ended input.

Note: this implies a maximum of eight double-ended inputs.

#### PPAIO-16/4 Analog Output Capacity

[DAQ_HRS_352_000]

The PPAIO-16/4 board shall provide 4 single-ended analog output channels.

#### PPAIO-16/4 ADC Input Voltage Range

[DAQ_HRS_353_000]

The PPAIO-16/4 board shall accept input voltages in the range 0-4.096V on the ADC input pins.

Note: this applies to both single-ended inputs and double-ended inputs

#### PPAIO-16/4 Analog Input Resolution (double-ended)

[DAQ_HRS_354_000]

The PPAIO-16/4 board shall support 16-bit 2's complement resolution on the analog inputs when using double-ended inputs.

Note: The ADC shall return negative values when the voltage on the double-ended negative input pin is greater than the voltage on the double-ended positive input pin.

#### PPAIO-16/4 Analog Input Resolution (single-ended)

[DAQ_HRS_355_000]

The PPAIO-16/4 board shall support 15-bit  analog inputs when using single-ended inputs.

Note: value is 0-0x7FFF (0-32767) based on a voltage input of 0-4.096 volts on the single-ended input.

#### PPAIO-16/4 Analog Input Precision (single-ended)

[DAQ_HRS_355_001]

The PPAIO-16/4 AIN0 port conversion value shall be accurate to within 5% of the actual input voltage.

[DAQ_HRS_355_002]

The PPAIO-16/4 AIN1 port conversion value shall be accurate to within 5% of the actual input voltage.

[DAQ_HRS_355_003]

The PPAIO-16/4 AIN2 port conversion value shall be accurate to within 5% of the actual input voltage.

[DAQ_HRS_355_004]

The PPAIO-16/4 AIN3 port conversion value shall be accurate to within 5% of the actual input voltage.

[DAQ_HRS_355_005]

The PPAIO-16/4 AIN4 port conversion value shall be accurate to within 5% of the actual input voltage.

[DAQ_HRS_355_006]

The PPAIO-16/4 AIN5 port conversion value shall be accurate to within 5% of the actual input voltage.

[DAQ_HRS_355_007]

The PPAIO-16/4 AIN6 port conversion value shall be accurate to within 5% of the actual input voltage.

[DAQ_HRS_355_008]

The PPAIO-16/4 AIN7 port conversion value shall be accurate to within 5% of the actual input voltage.

[DAQ_HRS_355_009]

The PPAIO-16/4 AIN8 port conversion value shall be accurate to within 5% of the actual input voltage.

[DAQ_HRS_355_010]

The PPAIO-16/4 AIN9 port conversion value shall be accurate to within 5% of the actual input voltage.

[DAQ_HRS_355_011]

The PPAIO-16/4 AIN10 port conversion value shall be accurate to within 5% of the actual input voltage.

[DAQ_HRS_355_012]

The PPAIO-16/4 AIN11 port conversion value shall be accurate to within 5% of the actual input voltage.

[DAQ_HRS_355_013]

The PPAIO-16/4 AIN12 port conversion value shall be accurate to within 5% of the actual input voltage.

[DAQ_HRS_355_014]

The PPAIO-16/4 AIN13 port conversion value shall be accurate to within 5% of the actual input voltage.

[DAQ_HRS_355_015]

The PPAIO-16/4 AIN14 port conversion value shall be accurate to within 5% of the actual input voltage.

[DAQ_HRS_355_016]

The PPAIO-16/4 AIN15 port conversion value shall be accurate to within 5% of the actual input voltage.

#### PPAIO-16/4 ADC Conversion Rate

[DAQ_HRS_356_000]

The PPAIO-16/4 board shall be capable of producing a minimum of 100 samples/sec.

#### PPAIO-16/4 Analog Output Capacity

[DAQ_HRS_357_000]

The PPAIO-16/4 board shall provide 4 singled-ended analog output channels.

#### PPAIO-16/4 DAC Output Voltage Range

[DAQ_HRS_358_000]

The PPAIO-16/4 board shall produce output voltages at least in the range ±5V on the DAC output pins.

[DAQ_HRS_358_001]

The AOUT0 output shall produce output voltages at least in the range ±5V on the AOUT0 output pins.

[DAQ_HRS_358_002]

The AOUT1 output shall produce output voltages at least in the range ±5V on the AOUT1 output pins.

[DAQ_HRS_358_003]

The AOUT2 output shall produce output voltages at least in the range ±5V on the AOUT2 output pins.

[DAQ_HRS_358_004]

The AOUT3 output shall produce output voltages at least in the range ±5V on the AOUT3 output pins.

#### PPAIO-16/4 Analog Output Resolution

[DAQ_HRS_359_000]

The PPAIO-16/4 board shall support 12-bit  analog outputs. Values in the range -2048 to +2047 produce a voltage at least in the range -5V to 5V.

#### PPAIO-16/4 DAC Conversion Rate

[DAQ_HRS_360_000]

The PPAIO-16/4 board shall be capable of producing a minimum of 100 output samples/sec.

#### PPAIO-16/4 Digital Input Connections

[DAQ_HRS_361_000]

The PPAIO-16/4 board shall provide a 6-pin (2x3) header accepting two sets of I2C control signals. The pinout is:

[DAQ_HRS_361_001]

1:	SDA (5V I2C port A data)

[DAQ_HRS_361_002]

2:	SDB (5V I2C port B data)

[DAQ_HRS_361_003]

3:	SCA (5V I2C port A clock)

[DAQ_HRS_361_004]

4:	SCB (5V I2C port B clock)

[DAQ_HRS_361_005]

5:	Gnd

[DAQ_HRS_361_006]

6:	Gnd

#### PPAIO-16/4 Digital Output Connections

[DAQ_HRS_362_000]

The PPAIO-16/4 board shall provide a 6-pin (2x3) header used to daisy-chain a second  PPAIO-16/4 board. The pin configuration of the header is similar to the digital input connection except that it swaps the pins for the two i2c busses. The pin out is:

[DAQ_HRS_362_001]

1:	SDB (5V I2C port B data)

[DAQ_HRS_362_002]

2:	SDA (5V I2C port A data)

[DAQ_HRS_362_003]

3:	SCB (5V I2C port B clock)

[DAQ_HRS_362_004]

4:	SCA (5V I2C port A clock)

[DAQ_HRS_362_005]

5:	Gnd

[DAQ_HRS_362_006]

6:	Gnd

Note: a maximum of two PPAIO-16/4 boards can be daisy-chained together using this scheme. Attempting to daisy-chain a third board reverts back to the A bus and creates address conflicts between the first and third boards.

#### PPAIO-16/4 Analog Input Connections

[DAQ_HRS_363_000]

The PPAIO-16/4 board shall provide 16 two-terminal screw terminals corresponding to inputs AIN0-AIN15 (analog inputs 0-15).

#### PPAIO-16/4 Analog Output Connections

[DAQ_HRS_364_000]

The PPAIO-16/4 board shall provide 4 two-terminal screw terminals corresponding to outputs AOUT0-AOUT3 (analog outputs 0-3).

#### PPAIO-16/4 ADC Modules

[DAQ_HRS_365_000]

The PPAIO-16/4 board shall support four Adafruit ADS1115 16-bit ADC modules.

#### PPAIO-16/4 Adafruit ADS1115 I2C Usage

[DAQ_HRS_366_000]

The four Adafruit ADS1115 16-bit ADC modules shall only use the first I2C signals on the digital input connection (pins 1 and 3 on the connector, SDA and SCA).

[DAQ_HRS_366_001]

The Adafruit ADS1115 16-bit ADC module controlling AOUT0-AOUT3 shall only use the first I2C signals on the digital input connection (pins 1 and 3 on the connector, SDA and SCA).

[DAQ_HRS_366_002]

The Adafruit ADS1115 16-bit ADC module controlling AOUT4-AOUT7 shall only use the first I2C signals on the digital input connection (pins 1 and 3 on the connector, SDA and SCA).

[DAQ_HRS_366_003]

The Adafruit ADS1115 16-bit ADC module controlling AOUT8-AOUT11 shall only use the first I2C signals on the digital input connection (pins 1 and 3 on the connector, SDA and SCA).

[DAQ_HRS_366_004]

The Adafruit ADS1115 16-bit ADC module controlling AOUT12-AOUT15 shall only use the first I2C signals on the digital input connection (pins 1 and 3 on the connector, SDA and SCA).

#### PPAIO-16/4 ADC Module #0 Address Selection

[DAQ_HRS_367_000]

The first Adafruit ADS1115 module shall be assigned address zero.

Note: Address zero is obtained by tying the ADDR pin to Gnd.

#### PPAIO-16/4 ADC Module #1 Connection to AIN0

[DAQ_HRS_368_000]

The first Adafruit ADS1115 module A0 input shall be connected to  the positive side of the AIN0 screw terminal.

#### PPAIO-16/4 ADC Module #1 Connection to AIN0 Ground

[DAQ_HRS_369_000]

The AIN0 screw terminal Gnd pin shall be connected to the analog ground associated with ADC module #1.

#### PPAIO-16/4 ADC Module #1 Connection to AIN1

[DAQ_HRS_370_000]

The first Adafruit ADS1115 module A1 input shall be connected to the positive side of the AIN1 screw terminal.

#### PPAIO-16/4 ADC Module #1 Connection to AIN1 Ground

[DAQ_HRS_371_000]

The AIN1 screw terminal Gnd pin shall be connected to the analog ground associated with ADC module #1.

#### PPAIO-16/4 ADC Module #1 Connection to AIN2

[DAQ_HRS_372_000]

The first Adafruit ADS1115 module A2 input shall be connected to the positive side of the AIN2 screw terminal.

#### PPAIO-16/4 ADC Module #1 Connection to AIN2 Ground

[DAQ_HRS_373_000]

The AIN2 screw terminal Gnd pin shall be connected to the analog ground associated with ADC module #1.

#### PPAIO-16/4 ADC Module #1 Connection to AIN3

[DAQ_HRS_374_000]

The first Adafruit ADS1115 module A3 input shall be connected to the positive side of the AIN3 screw terminal.

#### PPAIO-16/4 ADC Module #1 Connection to AIN3 Ground

[DAQ_HRS_375_000]

The AIN3 screw terminal Gnd pin shall be connected to the analog ground associated with ADC module #1.

#### PPAIO-16/4 ADC Module #2 Address Selection

[DAQ_HRS_376_000]

The second Adafruit ADS1115 module shall be assigned address one.

Note: Address one is obtained by tying the ADDR pin to +5V.

#### PPAIO-16/4 ADC Module #2 Connection to AIN0

[DAQ_HRS_377_000]

The first Adafruit ADS1115 module A0 input shall be connected to  the positive side of the AIN4 screw terminal.

#### PPAIO-16/4 ADC Module #2 Connection to AIN4 Ground

[DAQ_HRS_378_000]

The AIN4 screw terminal Gnd pin shall be connected to the analog ground associated with ADC module #2.

#### PPAIO-16/4 ADC Module #2 Connection to AIN5

[DAQ_HRS_379_000]

The first Adafruit ADS1115 module A1 input shall be connected to the positive side of the AIN5 screw terminal.

#### PPAIO-16/4 ADC Module #2 Connection to AIN5 Ground

[DAQ_HRS_380_000]

The AIN5 screw terminal Gnd pin shall be connected to the analog ground associated with ADC module #2.

#### PPAIO-16/4 ADC Module #2 Connection to AIN6

[DAQ_HRS_381_000]

The first Adafruit ADS1115 module A2 input shall be connected to the positive side of the AIN6 screw terminal.

#### PPAIO-16/4 ADC Module #2 Connection to AIN6 Ground

[DAQ_HRS_382_000]

The AIN6 screw terminal Gnd pin shall be connected to the analog ground associated with ADC module #2.

#### PPAIO-16/4 ADC Module #2 Connection to AIN7

[DAQ_HRS_383_000]

The first Adafruit ADS1115 module A3 input shall be connected to the positive side of the AIN7 screw terminal.

#### PPAIO-16/4 ADC Module #2 Connection to AIN7 Ground

[DAQ_HRS_384_000]

The AIN7 screw terminal Gnd pin shall be connected to the analog ground associated with ADC module #2.

#### PPAIO-16/4 ADC Module #3 Address Selection

[DAQ_HRS_385_000]

The third Adafruit ADS1115 module shall be assigned address two.

Note: Address two is obtained by tying the ADDR pin to SDA on ADC Module #3.

#### PPAIO-16/4 ADC Module #3 Connection to AIN8

[DAQ_HRS_386_000]

The first Adafruit ADS1115 module A0 input shall be connected to  the positive side of the AIN8 screw terminal.

#### PPAIO-16/4 ADC Module #3 Connection to AIN8 Ground

[DAQ_HRS_387_000]

The AIN8 screw terminal Gnd pin shall be connected to the analog ground associated with ADC module #3.

#### PPAIO-16/4 ADC Module #3 Connection to AIN9

[DAQ_HRS_388_000]

The first Adafruit ADS1115 module A1 input shall be connected to the positive side of the AIN9 screw terminal.

#### PPAIO-16/4 ADC Module #3 Connection to AIN9 Ground

[DAQ_HRS_389_000]

The AIN9 screw terminal Gnd pin shall be connected to the analog ground associated with ADC module #3.

#### PPAIO-16/4 ADC Module #3 Connection to AIN10

[DAQ_HRS_390_000]

The first Adafruit ADS1115 module A2 input shall be connected to the positive side of the AIN10 screw terminal.

#### PPAIO-16/4 ADC Module #3 Connection to AIN10 Ground

[DAQ_HRS_391_000]

The AIN10 screw terminal Gnd pin shall be connected to the analog ground associated with ADC module #3.

#### PPAIO-16/4 ADC Module #3 Connection to AIN11

[DAQ_HRS_392_000]

The first Adafruit ADS1115 module A3 input shall be connected to the positive side of the AIN11 screw terminal.

#### PPAIO-16/4 ADC Module #3 Connection to AIN11 Ground

[DAQ_HRS_393_000]

The AIN11 screw terminal Gnd pin shall be connected to the analog ground associated with ADC module #3.

#### PPAIO-16/4 ADC Module #4 Address Selection

[DAQ_HRS_394_000]

The fourth Adafruit ADS1115 module shall be assigned address three.

Note: Address three is obtained by tying the ADDR pin to SCL on ADC Module #4.

#### PPAIO-16/4 ADC Module #4 Connection to AIN12

[DAQ_HRS_395_000]

The first Adafruit ADS1115 module A0 input shall be connected to  the positive side of the AIN12 screw terminal.

#### PPAIO-16/4 ADC Module #4 Connection to AIN2 Ground

[DAQ_HRS_396_000]

The AIN12 screw terminal Gnd pin shall be connected to the analog ground associated with ADC module #4.

#### PPAIO-16/4 ADC Module #4 Connection to AIN13

[DAQ_HRS_397_000]

The first Adafruit ADS1115 module A1 input shall be connected to the positive side of the AIN13 screw terminal.

#### PPAIO-16/4 ADC Module #4 Connection to AIN13 Ground

[DAQ_HRS_398_000]

The AIN13 screw terminal Gnd pin shall be connected to the analog ground associated with ADC module #4.

#### PPAIO-16/4 ADC Module #4 Connection to AIN14

[DAQ_HRS_399_000]

The first Adafruit ADS1115 module A2 input shall be connected to the positive side of the AIN14 screw terminal.

#### PPAIO-16/4 ADC Module #4 Connection to AIN14 Ground

[DAQ_HRS_400_000]

The AIN14 screw terminal Gnd pin shall be connected to the analog ground associated with ADC module #4.

#### PPAIO-16/4 ADC Module #4 Connection to AIN15

[DAQ_HRS_401_000]

The first Adafruit ADS1115 module A3 input shall be connected to the positive side of the AIN15 screw terminal.

#### PPAIO-16/4 ADC Module #4 Connection to AIN15 Ground

[DAQ_HRS_402_000]

The AIN15 screw terminal Gnd pin shall be connected to the analog ground associated with ADC module #4.

#### PPAIO-16/4 DAC I2C Module Addresses (Daisy-Chaining)

[DAQ_HRS_403_000]

When daisy-chaining two PPAIO-16/4, one board shall be populated with Adafruit MCP4725 DAC breakout boards and the second shall be populated with Sparkfun MCP4725 breakout boards.

The MCP4725 DAC chip (used on the Adafruit and Sparkfun MCP4725 breakout boards) only support two programmable addresses. Fortunately, the chips used by Adafruit and Sparkfun have different base I2C addresses (Adafruit = 0x62/0x63 and Sparkfun = 0x60/0x61). Therefore, by using breakout boards from the two different vendors it is possible to place 8 DACs on two I2C busses.

#### PPAIO-16/4 DAC Selection on First PPAIO-16/4

[DAQ_HRS_404_000]

The first board in a pair of daisy-chained PPAIO-16/4 boards shall be populated with four Adafruit MCP4725 breakout boards.

#### PPAIO-16/4 DAC Selection on Second (in a daisy chain) PPAIO-16/4

[DAQ_HRS_405_000]

The second board in a pair of daisy-chained PPAIO-16/4 boards shall be populated with four Sparkfun MCP4725 breakout boards.

#### PPAIO-16/4 DAC #0 I2C Bus Selection on First (in a daisy chain) PPAIO-16/4

[DAQ_HRS_406_000]

DAC #0 (AOUT0) shall be connected to the "A" I2C bus on the PPAIO-16/4 Digital Input Connection (see [DAQ_HRS_362_000]).

#### PPAIO-16/4 DAC #0 I2C Address Selection on First (in a daisy chain) PPAIO-16/4

[DAQ_HRS_407_000]

Adafruit DAC #0 (AOUT0) shall be have the ADDR pin tied to Gnd (I2C address=0x62, this is the default if the pin is left floating).

#### PPAIO-16/4 DAC #1 I2C Bus Selection on First (in a daisy chain) PPAIO-16/4

[DAQ_HRS_408_000]

DAC #1 (AOUT1) shall be connected to the "A" I2C bus on the PPAIO-16/4 Digital Input Connection (see [DAQ_HRS_362_000]).

#### PPAIO-16/4 DAC #1 I2C Bus Selection on First (in a daisy chain) PPAIO-16/4

[DAQ_HRS_409_000]

Adafruit DAC #1 (AOUT1) shall be have the ADDR pin tied to Vcc (I2C address=0x63).

#### PPAIO-16/4 DAC #2 I2C Bus Selection on First (in a daisy chain) PPAIO-16/4

[DAQ_HRS_410_000]

DAC #2 (AOUT2) shall be connected to the "B" I2C bus on the PPAIO-16/4 Digital Input Connection (see [DAQ_HRS_362_000]).

#### PPAIO-16/4 DAC #2 I2C Address Selection on First (in a daisy chain) PPAIO-16/4

[DAQ_HRS_411_000]

Adafruit DAC #2 (AOUT2) shall be have the ADDR pin tied to Gnd (I2C address=0x62, this is the default if the pin is left floating).

#### PPAIO-16/4 DAC #3 I2C Bus Selection on First (in a daisy chain) PPAIO-16/4

[DAQ_HRS_412_000]

DAC #3 (AOUT3) shall be connected to the "B" I2C bus on the PPAIO-16/4 Digital Input Connection (see [DAQ_HRS_362_000]).

#### PPAIO-16/4 DAC #3 I2C Bus Selection on First (in a daisy chain) PPAIO-16/4

[DAQ_HRS_413_000]

Adafruit DAC #3 (AOUT3) shall be have the ADDR pin tied to Vcc (I2C address=0x63).

#### PPAIO-16/4 DAC #0 I2C Bus Selection on Second (in a daisy chain) PPAIO-16/4

[DAQ_HRS_414_000]

DAC #0 (AOUT0) shall be connected to the "A" I2C bus on the PPAIO-16/4 Digital Input Connection (see [DAQ_HRS_362_000]).

#### PPAIO-16/4 DAC #0 I2C Address Selection on Second (in a daisy chain) PPAIO-16/4

[DAQ_HRS_415_000]

Sparkfun DAC #0 (AOUT0) shall be have the A0 pin tied to Gnd (I2C address=0x60, this is the default if the pin is left floating).

#### PPAIO-16/4 DAC #1 I2C Bus Selection on Second (in a daisy chain) PPAIO-16/4

[DAQ_HRS_416_000]

DAC #1 (AOUT1) shall be connected to the "A" I2C bus on the PPAIO-16/4 Digital Input Connection (see [DAQ_HRS_362_000]).

#### PPAIO-16/4 DAC #1 I2C Bus Selection on Second (in a daisy chain) PPAIO-16/4

[DAQ_HRS_417_000]

Sparkfun DAC #1 (AOUT1) shall be have the A0 pin tied to Vcc (I2C address=0x61).

#### PPAIO-16/4 DAC #2 I2C Bus Selection on Second (in a daisy chain) PPAIO-16/4

[DAQ_HRS_418_000]

DAC #2 (AOUT2) shall be connected to the "B" I2C bus on the PPAIO-16/4 Digital Input Connection (see [DAQ_HRS_362_000]).

#### PPAIO-16/4 DAC #2 I2C Address Selection on Second (in a daisy chain) PPAIO-16/4

[DAQ_HRS_419_000]

Sparkfun DAC #2 (AOUT2) shall be have the A0 pin tied to Gnd (I2C address=0x60, this is the default if the pin is left floating).

#### PPAIO-16/4 DAC #3 I2C Bus Selection on Second (in a daisy chain) PPAIO-16/4

[DAQ_HRS_420_000]

DAC #3 (AOUT3) shall be connected to the "B" I2C bus on the PPAIO-16/4 Digital Input Connection (see [DAQ_HRS_362_000]).

#### PPAIO-16/4 DAC #3 I2C Bus Selection on Second (in a daisy chain) PPAIO-16/4

[DAQ_HRS_421_000]

Sparkfun DAC #3 (AOUT3) shall be have the A0 pin tied to Vcc (I2C address=0x61).

#### PPAIO-16/4 Power Supply Connection

[DAQ_HRS_422_000]

The PPAIO-16/4 board shall provide a three-pin screw terminal connector (5mm centers) to accept ±12V/Gnd from an external power supply

#### PPAIO-16/4 Clean Power Supply

[DAQ_HRS_423_000]

The power supply connected to the PPAIO-16/4 shall be a "clean" analog-only power supply that does not power digital boards or other noisy devices.

#### PPAIO-16/4 Power Supply LED

[DAQ_HRS_424_000]

The PPAIO-16/4board shall provide an LED that is illuminated whenever power is applied to the board.

#### PPAIO-16/4 Output Voltage Conversion

[DAQ_HRS_425_000]

The PPAIO-16/4board shall provide four analog amplifier channels to convert the 0-5V output from the DAC to the range ±5V.

[DAQ_HRS_425_001]

The PPAIO-16/4board shall provide an analog amplifier channel to convert the 0-5V output from the DAC AOUT0 to the range ±5V.

[DAQ_HRS_425_002]

The PPAIO-16/4board shall provide an analog amplifier channel to convert the 0-5V output from the DAC AOUT1 to the range ±5V.

[DAQ_HRS_425_003]

The PPAIO-16/4board shall provide an analog amplifier channel to convert the 0-5V output from the DAC AOUT2 to the range ±5V.

[DAQ_HRS_425_004]

The PPAIO-16/4board shall provide an analog amplifier channel to convert the 0-5V output from the DAC AOUT3 to the range ±5V.

[DAQ_HRS_425_005]

The PPAIO-16/4board shall provide an analog amplifier channel to convert the 0-5V output from the DAC AOUT0 to the range ±10V via a jumper option.

[DAQ_HRS_425_006]

The PPAIO-16/4board shall provide an analog amplifier channel to convert the 0-5V output from the DAC AOUT1 to the range ±10V via a jumper option.

[DAQ_HRS_425_007]

The PPAIO-16/4board shall provide an analog amplifier channel to convert the 0-5V output from the DAC AOUT2 to the range ±10V via a jumper option.

[DAQ_HRS_425_008]

The PPAIO-16/4board shall provide an analog amplifier channel to convert the 0-5V output from the DAC AOUT3 to the range ±10V via a jumper option.

#### PPAIO-16/4 Linear Conversion

[DAQ_HRS_426_000]

The transfer function for the analog conversion shall be linear.

#### PPAIO-16/4 Span/Gain Adjustment

[DAQ_HRS_427_000]

The PPAIO-16/4 board shall provide a multi-turn potentiometer (on each DAC output channel) that allows a technician to adjust the gain (span) of an output signal.

#### PPAIO-16/4 Zero Adjustment

[DAQ_HRS_428_000]

The PPAIO-16/4 board shall provide a multi-turn potentiometer (on each DAC output channel) that allows a technician to adjust the zero point (offset) of an output signal.

#### PPAIO-16/4 Frequency Response

[DAQ_HRS_429_000]

Each output channel on the PPAIO-16/4 board shall have a frequency response of at least 1kHz.

### PPAC-4 4-Channel Analog Conditioning Board

#### PPAC-4 Capacity

[DAQ_HRS_450_000]

The PPAC-4 board shall provide 4 channels of analog conditioning.

#### PPAC-4 Power Supply Connection

[DAQ_HRS_451_000]

The PPAC-4 board shall provide a three-pin screw terminal connector (5mm centers) to accept ±12V/Gnd from an external power supply

#### PPAC-4 Power Supply LED

[DAQ_HRS_452_000]

The PPAC-4 board shall provide an LED that is illuminated whenever power is applied to the board (+12V).

#### PPAC-4 Clean Power Supply

[DAQ_HRS_453_000]

The power supply connected to the PPAC-4 shall be a "clean" analog-only power supply that does not power digital boards or other noisy devices.

#### PPAC-4 Signal Isolation

[DAQ_HRS_454_000]

Each analog input channel shall provide an isolation amplifier that isolates the analog input signal from the DAQ boards as well as isolating the input signal from other analog signals.

#### PPAC-4 Power Supply Isolation

[DAQ_HRS_455_000]

Each analog input channel shall provide an isolated power supply for each isolation amplifier.

#### PPAC-4 Maximum Input Voltage Range

[DAQ_HRS_456_000]

Each analog input channel shall accept inputs in the range ±10V.

#### PPAC-4 Double-ended Output

[DAQ_HRS_457_000]

Each analog channel shall produce a pair of double-ended outputs,

[DAQ_HRS_457_001]

whose output voltage is in the range 0-4.096V.

#### PPAC-4 Double-ended Output from Positive/Zero Inputs

[DAQ_HRS_458_000]

Each analog channel shall produce a positive (or zero) voltage on the positive terminal that is greater than the positive (or zero) output on the negative terminal.

Note: for double-ended outputs, the resulting value is the difference between the positive and negative output terminals – both of which are positive voltages.

#### PPAC-4 Double-ended Output from Negative Inputs

[DAQ_HRS_459_000]

Each analog channel shall produce a positive (or zero) voltage on the positive terminal that is less than the positive (or zero) output on the negative terminal.

Note: for double-ended outputs, the resulting value is the difference between the positive and negative output terminals – both of which are positive voltages.

#### PPAC-4 Linear Conversion

[DAQ_HRS_460_000]

The transfer function for the analog conversion shall be linear.

#### PPAC-4 Span/Gain Adjustment

[DAQ_HRS_461_000]

The PPAC-4 board shall provide a multi-turn potentiometer (on each channel) that allows a technician to adjust the gain (span) of an input signal.

Note: the span adjustment is intended for minor gain tweaks when calibrating the device at site. The Adafruit ADS1115 module provides a programmable gain amplifier than the software can use to handle larger gain adjustments (such as ±5V inputs rather than ±10V) to avoid losing resolution in the ADC.

#### PPAC-4 Zero Adjustment

[DAQ_HRS_462_000]

The PPAC-4 board shall provide a multi-turn potentiometer (on each channel) that allows a technician to adjust the zero point (offset) of an input signal.

#### PPAC-4 VRef Adjustment

[DAQ_HRS_463_000]

The PPAC-4 board shall provide a multi-turn potentiometer (on each channel) that allows a technician to adjust the voltage reference point (the cross-over point between the two legs of the differential/doubled-ended output).

Note: This is usually set to ½ of the maximum output voltage (4.096V is the typical maximum output voltage, so VRef is typically set to 2.048V).

#### PPAC-4 Analog Input Terminals

[DAQ_HRS_464_000]

The PPAC-4 board shall provide 4 two-pin screw terminals to connect an input voltage to the input pins on each channel's isolation amplifier.

#### PPAC-4 Single-ended Inputs

[DAQ_HRS_465_000]

Each input channel on the PPAC-4 board shall be a single-ended input (voltage input + Gnd).

#### PPAC-4 Analog Output Terminals

[DAQ_HRS_466_000]

The PPAC-4 board shall provide 4 two-pin screw terminals to connect the double-ended output to an external device (such as  PPAIO-16/4 board).

#### PPAC-4 Frequency Response

[DAQ_HRS_467_000]

Each channel on the PPAC-4 board shall have a frequency response of at least 1kHz.

### 12-Channel Relay-based Digital I/O Board (PPRlyio-12)

#### PPRLYIO-12 Capacity

[DAQ_HRS_500_000]

The PPRLYIO-12 shall provide 12 bits of relay digital I/O.

#### PPRLYIO-12 Power Supply Connection

[DAQ_HRS_501_000]

The PPRLYIO-12  board shall provide a two-pin screw terminal connector (5mm centers) to accept 5V/Gnd from an external power supply

#### PPRLYIO-12 Power Supply LED

[DAQ_HRS_502_000]

The PPRLYIO-12  board shall provide an LED that is illuminated whenever power is applied to the board.

#### PPRLYIO-12 Output Connector Pinout

[DAQ_HRS_503_000]

The PPRLYIO-12 board shall provide a 20-pin (2x10) header that is compatible with the PPDIO96 bank pinouts, using the following pinout:

- Bit 1

- Bit 0

- Bit 2

- Gnd

- Bit 3

- Gnd

- Bit 4

- Gnd

- Bit 5

- Gnd

- Bit 6

- Gnd

- Bit 7

- Gnd

- Bit 8

- Gnd

- Bit 9

- Gnd

- Bit 10

- Bit 11

[DAQ_HRS_503_001]

1:	Bit 1

[DAQ_HRS_503_002]

2:	Bit 0

[DAQ_HRS_503_003]

3:	Bit 2

[DAQ_HRS_503_004]

4:	Gnd

[DAQ_HRS_503_005]

5:	Bit 3

[DAQ_HRS_503_006]

6:	Gnd

[DAQ_HRS_503_007]

7:	Bit 4

[DAQ_HRS_503_008]

8:	Gnd

[DAQ_HRS_503_009]

9:	Bit 5

[DAQ_HRS_503_010]

10:	Gnd

[DAQ_HRS_503_011]

11:	Bit 6

[DAQ_HRS_503_012]

12:	Gnd

[DAQ_HRS_503_013]

13:	Bit 7

[DAQ_HRS_503_014]

14:	Gnd

[DAQ_HRS_503_015]

15:	Bit 8

[DAQ_HRS_503_016]

16:	Gnd

[DAQ_HRS_503_017]

17:	Bit 9

[DAQ_HRS_503_018]

18:	Gnd

[DAQ_HRS_503_019]

19:	Bit 10

[DAQ_HRS_503_020]

20:	Bit 11

Note: Gnd pins are all connected to the same ground plane.

#### PPRLYIO-12 Input Connector Pinout

[DAQ_HRS_504_000]

The PPRLYIO-12 board shall provide a 20-pin (2x10) header that is compatible with the PPDIO96 bank pinouts, using the same pinout as in [DAQ_HRS_503].

[DAQ_HRS_504_001]

1:	Bit 1

[DAQ_HRS_504_002]

2:	Bit 0

[DAQ_HRS_504_003]

3:	Bit 2

[DAQ_HRS_504_004]

4:	Gnd

[DAQ_HRS_504_005]

5:	Bit 3

[DAQ_HRS_504_006]

6:	Gnd

[DAQ_HRS_504_007]

7:	Bit 4

[DAQ_HRS_504_008]

8:	Gnd

[DAQ_HRS_504_009]

9:	Bit 5

[DAQ_HRS_504_010]

10:	Gnd

[DAQ_HRS_504_011]

11:	Bit 6

[DAQ_HRS_504_012]

12:	Gnd

[DAQ_HRS_504_013]

13:	Bit 7

[DAQ_HRS_504_014]

14:	Gnd

[DAQ_HRS_504_015]

15:	Bit 8

[DAQ_HRS_504_016]

16:	Gnd

[DAQ_HRS_504_017]

17:	Bit 9

[DAQ_HRS_504_018]

18:	Gnd

[DAQ_HRS_504_019]

19:	Bit 10

[DAQ_HRS_504_020]

20:	Bit 11

#### PPRLYIO-12 Signal LEDs

[DAQ_HRS_505_000]

The PPRLYIO-12 board shall provide 12 signal LEDs.

#### PPRLYIO-12 Signal LED #0 Illumination

[DAQ_HRS_506_000]

Signal LED #0 on the PPRLYIO-12 board shall illuminate when input D0 is active.

#### PPRLYIO-12 Signal LED #1 Illumination

[DAQ_HRS_507_000]

Signal LED #1 on the PPRLYIO-12 board shall illuminate when input D1 is active.

#### PPRLYIO-12 Signal LED #2 Illumination

[DAQ_HRS_508_000]

Signal LED #2 on the PPRLYIO-12 board shall illuminate when input D2 is active.

#### PPRLYIO-12 Signal LED #3 Illumination

[DAQ_HRS_509_000]

Signal LED #3 on the PPRLYIO-12 board shall illuminate when input D3 is active.

#### PPRLYIO-12 Signal LED #4 Illumination

[DAQ_HRS_510_000]

Signal LED #4 on the PPRLYIO-12 board shall illuminate when input D4 is active.

#### PPRLYIO-12 Signal LED #5 Illumination

[DAQ_HRS_511_000]

Signal LED #5 on the PPRLYIO-12 board shall illuminate when input D5 is active.

#### PPRLYIO-12 Signal LED #6 Illumination

[DAQ_HRS_512_000]

Signal LED #6 on the PPRLYIO-12 board shall illuminate when input D6 is active.

#### PPRLYIO-12 Signal LED #7 Illumination

[DAQ_HRS_213_000]

Signal LED #7 on the PPRLYIO-12 board shall illuminate when input D7 is active.

#### PPRLYIO-12 Signal LED #8 Illumination

[DAQ_HRS_514_000]

Signal LED #8 on the PPRLYIO-12 board shall illuminate when input D8 is active.

#### PPRLYIO-12 Signal LED #9 Illumination

[DAQ_HRS_515_000]

Signal LED #9 on the PPRLYIO-12 board shall illuminate when input D9 is active.

#### PPRLYIO-12 Signal LED #10 Illumination

[DAQ_HRS_516_000]

Signal LED #10 on the PPRLYIO-12 board shall illuminate when input D10 is active.

#### PPRLYIO-12 Signal LED #11 Illumination

[DAQ_HRS_517_000]

Signal LED #11 on the PPRLYIO-12 board shall illuminate when input D11 is active.

#### PPRLYIO-12 Input Polarity Selection

[DAQ_HRS_518_000]

Each input channel on the PPRlyio-12 board shall provide a jumper to select active high or active low operation.

#### PPRLYIO-12 Output Pullup Resistor Selection

[DAQ_HRS_519_000]

Each output channel on the PPRlyio-12 board shall provide a jumper to open collector or TTL-level (via pullup resistor) operation.

#### PPRLYIO-12 D0 Pullup Resistor Selection

[DAQ_HRS_519_001]

Pullups jumper #0 shall provide a +5V pullup voltage to the DOUT 0 output.

#### PPRLYIO-12 D1 Pullup Resistor Selection

[DAQ_HRS_519_002]

Pullups jumper #1 shall provide a +5V pullup voltage to the DOUT 1 output.

#### PPRLYIO-12 D2 Pullup Resistor Selection

[DAQ_HRS_519_003]

Pullups jumper #2 shall provide a +5V pullup voltage to the DOUT 2 output.

#### PPRLYIO-12 D3 Pullup Resistor Selection

[DAQ_HRS_519_004]

Pullups jumper #3 shall provide a +5V pullup voltage to the DOUT 3 output.

#### PPRLYIO-12 D4 Pullup Resistor Selection

[DAQ_HRS_519_005]

Pullups jumper #4 shall provide a +5V pullup voltage to the DOUT 4 output.

#### PPRLYIO-12 D5 Pullup Resistor Selection

[DAQ_HRS_519_006]

Pullups jumper #5 shall provide a +5V pullup voltage to the DOUT 5 output.

#### PPRLYIO-12 D6 Pullup Resistor Selection

[DAQ_HRS_519_007]

Pullups jumper #6 shall provide a +5V pullup voltage to the DOUT 6 output.

#### PPRLYIO-12 D7 Pullup Resistor Selection

[DAQ_HRS_519_008]

Pullups jumper #7 shall provide a +5V pullup voltage to the DOUT 7 output.

#### PPRLYIO-12 D8 Pullup Resistor Selection

[DAQ_HRS_519_009]

Pullups jumper #8 shall provide a +5V pullup voltage to the DOUT 8 output.

#### PPRLYIO-12 D9 Pullup Resistor Selection

[DAQ_HRS_519_010]

Pullups jumper #9 shall provide a +5V pullup voltage to the DOUT 9 output.

#### PPRLYIO-12 D10 Pullup Resistor Selection

[DAQ_HRS_519_011]

Pullups jumper #10 shall provide a +5V pullup voltage to the DOUT 10 output.

#### PPRLYIO-12 D11 Pullup Resistor Selection

[DAQ_HRS_519_012]

Pullups jumper #11 shall provide a +5V pullup voltage to the DOUT 11 output.

#### PPRELAY12 Output Isolation

[DAQ_HRS_520_000]

The PPRlyio-12 board shall provide isolation for all relay outputs.

Note: this feature is provided by default given the nature of mechanical relays.

#### PPRELAY12 Output Current Capacity

[DAQ_HRS_521_000]

The PPRlyio-12 board shall be capable of handling an minimum of 2A on each output channel.

#### PPRELAY12 Output Voltage Capacity

[DAQ_HRS_522_000]

The PPRlyio-12 board shall be capable of handling a minimum of  30VDC on each output channel.

#### PPRELAY12 Output Connectors

[DAQ_HRS_523_000]

The PPRlyio-12 board shall provide a three-pin screw terminal for each relay output (5mm centers) for NC/COM/NO relay connections.

[DAQ_HRS_523_001]

With polarity jumper #0 in the non-inverting (0) position, the D0 relay on the PPRLYIO-12 board shall have the NC/COM contacts closed when DIN0-11 pin #2 is high.

[DAQ_HRS_523_002]

With polarity jumper #0 in the non-inverting (0) position, the D0 relay on the PPRLYIO-12 board shall have the NO/COM contacts open when DIN0-11 pin #2 is high.

[DAQ_HRS_523_003]

With polarity jumper #0 in the non-inverting (0) position, the D0 relay on the PPRLYIO-12 board shall have the NC/COM contacts open when DIN0-11 pin #2 is low.

[DAQ_HRS_523_004]

With polarity jumper #0 in the non-inverting (0) position, the D0 relay on the PPRLYIO-12 board shall have the NO/COM contacts closed when DIN0-11 pin #2 is low.

[DAQ_HRS_523_005]

With polarity jumper #1 in the non-inverting (0) position, the D1 relay on the PPRLYIO-12 board shall have the NC/COM contacts closed when DIN0-11 pin #1 is high.

[DAQ_HRS_523_006]

With polarity jumper #1 in the non-inverting (0) position, the D1 relay on the PPRLYIO-12 board shall have the NO/COM contacts open when DIN0-11 pin #1 is high.

[DAQ_HRS_523_007]

With polarity jumper #1 in the non-inverting (0) position, the D1 relay on the PPRLYIO-12 board shall have the NC/COM contacts open when DIN0-11 pin #1 is low.

[DAQ_HRS_523_008]

With polarity jumper #1 in the non-inverting (0) position, the D1 relay on the PPRLYIO-12 board shall have the NO/COM contacts closed when DIN0-11 pin #1 is low.

[DAQ_HRS_523_009]

With polarity jumper #2 in the non-inverting (0) position, the D2 relay on the PPRLYIO-12 board shall have the NC/COM contacts closed when DIN0-11 pin #3 is high.

[DAQ_HRS_523_010]

With polarity jumper #2 in the non-inverting (0) position, the D2 relay on the PPRLYIO-12 board shall have the NO/COM contacts open when DIN0-11 pin #3 is high.

[DAQ_HRS_523_011]

With polarity jumper #2 in the non-inverting (0) position, the D2 relay on the PPRLYIO-12 board shall have the NC/COM contacts open when DIN0-11 pin #3 is low.

[DAQ_HRS_523_012]

With polarity jumper #2 in the non-inverting (0) position, the D2 relay on the PPRLYIO-12 board shall have the NO/COM contacts closed when DIN0-11 pin #3 is low.

[DAQ_HRS_523_013]

With polarity jumper #3 in the non-inverting (0) position, the D3 relay on the PPRLYIO-12 board shall have the NC/COM contacts closed when DIN0-11 pin #5 is high.

[DAQ_HRS_523_014]

With polarity jumper #3 in the non-inverting (0) position, the D3 relay on the PPRLYIO-12 board shall have the NO/COM contacts open when DIN0-11 pin #5 is high.

[DAQ_HRS_523_015]

With polarity jumper #3 in the non-inverting (0) position, the D3 relay on the PPRLYIO-12 board shall have the NC/COM contacts open when DIN0-11 pin #5 is low.

[DAQ_HRS_523_016]

With polarity jumper #3 in the non-inverting (0) position, the D3 relay on the PPRLYIO-12 board shall have the NO/COM contacts closed when DIN0-11 pin #5 is low.

[DAQ_HRS_523_017]

With polarity jumper #4 in the non-inverting (0) position, the D4 relay on the PPRLYIO-12 board shall have the NC/COM contacts closed when DIN0-11 pin #7 is high.

[DAQ_HRS_523_018]

With polarity jumper #4 in the non-inverting (0) position, the D4 relay on the PPRLYIO-12 board shall have the NO/COM contacts open when DIN0-11 pin #7 is high.

[DAQ_HRS_523_019]

With polarity jumper #4 in the non-inverting (0) position, the D4 relay on the PPRLYIO-12 board shall have the NC/COM contacts open when DIN0-11 pin #7 is low.

[DAQ_HRS_523_020]

With polarity jumper #4 in the non-inverting (0) position, the D4 relay on the PPRLYIO-12 board shall have the NO/COM contacts closed when DIN0-11 pin #7 is low.

[DAQ_HRS_523_021]

With polarity jumper #5 in the non-inverting (0) position, the D5 relay on the PPRLYIO-12 board shall have the NC/COM contacts closed when DIN0-11 pin #9 is high.

[DAQ_HRS_523_022]

With polarity jumper #5 in the non-inverting (0) position, the D5 relay on the PPRLYIO-12 board shall have the NO/COM contacts open when DIN0-11 pin #9 is high.

[DAQ_HRS_523_023]

With polarity jumper #5 in the non-inverting (0) position, the D5 relay on the PPRLYIO-12 board shall have the NC/COM contacts open when DIN0-11 pin #9 is low.

[DAQ_HRS_523_024]

With polarity jumper #5 in the non-inverting (0) position, the D5 relay on the PPRLYIO-12 board shall have the NO/COM contacts closed when DIN0-11 pin #9 is low.

[DAQ_HRS_523_025]

With polarity jumper #6 in the non-inverting (0) position, the D6 relay on the PPRLYIO-12 board shall have the NC/COM contacts closed when DIN0-11 pin #11 is high.

[DAQ_HRS_523_026]

With polarity jumper #6 in the non-inverting (0) position, the D6 relay on the PPRLYIO-12 board shall have the NO/COM contacts open when DIN0-11 pin #11 is high.

[DAQ_HRS_523_027]

With polarity jumper #6 in the non-inverting (0) position, the D6 relay on the PPRLYIO-12 board shall have the NC/COM contacts open when DIN0-11 pin #11 is low.

[DAQ_HRS_523_028]

With polarity jumper #6 in the non-inverting (0) position, the D6 relay on the PPRLYIO-12 board shall have the NO/COM contacts closed when DIN0-11 pin #11 is low.

[DAQ_HRS_523_029]

With polarity jumper #7 in the non-inverting (0) position, the D7 relay on the PPRLYIO-12 board shall have the NC/COM contacts closed when DIN0-11 pin #13 is high.

[DAQ_HRS_523_030]

With polarity jumper #7 in the non-inverting (0) position, the D7 relay on the PPRLYIO-12 board shall have the NO/COM contacts open when DIN0-11 pin #13 is high.

[DAQ_HRS_523_031]

With polarity jumper #7 in the non-inverting (0) position, the D7 relay on the PPRLYIO-12 board shall have the NC/COM contacts open when DIN0-11 pin #13 is low.

[DAQ_HRS_523_032]

With polarity jumper #7 in the non-inverting (0) position, the D7 relay on the PPRLYIO-12 board shall have the NO/COM contacts closed when DIN0-11 pin #13 is low.

[DAQ_HRS_523_033]

With polarity jumper #8 in the non-inverting (0) position, the D8 relay on the PPRLYIO-12 board shall have the NC/COM contacts closed when DIN0-11 pin #15 is high.

[DAQ_HRS_523_034]

With polarity jumper #8 in the non-inverting (0) position, the D8 relay on the PPRLYIO-12 board shall have the NO/COM contacts open when DIN0-11 pin #15 is high.

[DAQ_HRS_523_035]

With polarity jumper #8 in the non-inverting (0) position, the D8 relay on the PPRLYIO-12 board shall have the NC/COM contacts open when DIN0-11 pin #15 is low.

[DAQ_HRS_523_036]

With polarity jumper #8 in the non-inverting (0) position, the D8 relay on the PPRLYIO-12 board shall have the NO/COM contacts closed when DIN0-11 pin #15 is low.

[DAQ_HRS_523_037]

With polarity jumper #9 in the non-inverting (0) position, the D9 relay on the PPRLYIO-12 board shall have the NC/COM contacts closed when DIN0-11 pin #17 is high.

[DAQ_HRS_523_038]

With polarity jumper #9 in the non-inverting (0) position, the D9 relay on the PPRLYIO-12 board shall have the NO/COM contacts open when DIN0-11 pin #17 is high.

[DAQ_HRS_523_039]

With polarity jumper #9 in the non-inverting (0) position, the D9 relay on the PPRLYIO-12 board shall have the NC/COM contacts open when DIN0-11 pin #17 is low.

[DAQ_HRS_523_040]

With polarity jumper #9 in the non-inverting (0) position, the D9 relay on the PPRLYIO-12 board shall have the NO/COM contacts closed when DIN0-11 pin #17 is low.

[DAQ_HRS_523_041]

With polarity jumper #10 in the non-inverting (0) position, the D10  relay on the PPRLYIO-12 board shall have the NC/COM contacts closed when DIN0-11 pin #19 is high.

[DAQ_HRS_523_042]

With polarity jumper #10 in the non-inverting (0) position, the D10  relay on the PPRLYIO-12 board shall have the NO/COM contacts open when DIN0-11 pin #19 is high.

[DAQ_HRS_523_043]

With polarity jumper #10  in the non-inverting (0) position, the D10 relay on the PPRLYIO-12 board shall have the NC/COM contacts open when DIN0-11 pin #19 is low.

[DAQ_HRS_523_044]

With polarity jumper #10 in the non-inverting (0) position, the D10 relay on the PPRLYIO-12 board shall have the NO/COM contacts closed when DIN0-11 pin #19 is low.

[DAQ_HRS_523_045]

With polarity jumper #11 in the non-inverting (0) position, the D11  relay on the PPRLYIO-12 board shall have the NC/COM contacts closed when DIN0-11 pin #20 is high.

[DAQ_HRS_523_046]

With polarity jumper #11 in the non-inverting (0) position, the D11  relay on the PPRLYIO-12 board shall have the NO/COM contacts open when DIN0-11 pin #20 is high.

[DAQ_HRS_523_047]

With polarity jumper #11  in the non-inverting (0) position, the D11 relay on the PPRLYIO-12 board shall have the NC/COM contacts open when DIN0-11 pin #20 is low.

[DAQ_HRS_523_048]

With polarity jumper #11 in the non-inverting (0) position, the D11 relay on the PPRLYIO-12 board shall have the NO/COM contacts closed when DIN0-11 pin #20 is low.

[DAQ_HRS_523_049]

With polarity jumper #0 in the inverting (1) position, the D0 relay on the PPRLYIO-12 board shall have the NC/COM contacts open when DIN0-11 pin #2 is high.

[DAQ_HRS_523_050]

With polarity jumper #0 in the inverting (1) position, the D0 relay on the PPRLYIO-12 board shall have the NO/COM contacts closed when DIN0-11 pin #2 is high.

[DAQ_HRS_523_051]

With polarity jumper #0 in the inverting (1) position, the D0 relay on the PPRLYIO-12 board shall have the NC/COM contacts closed when DIN0-11 pin #2 is low.

[DAQ_HRS_523_052]

With polarity jumper #0 in the inverting (1) position, the D0 relay on the PPRLYIO-12 board shall have the NO/COM contacts open when DIN0-11 pin #2 is low.

[DAQ_HRS_523_053]

With polarity jumper #1 in the inverting (1) position, the D1 relay on the PPRLYIO-12 board shall have the NC/COM contacts open when DIN0-11 pin #1 is high.

[DAQ_HRS_523_054]

With polarity jumper #1 in the inverting (1) position, the D1 relay on the PPRLYIO-12 board shall have the NO/COM contacts closed when DIN0-11 pin #1 is high.

[DAQ_HRS_523_055]

With polarity jumper #1 in the inverting (1) position, the D1 relay on the PPRLYIO-12 board shall have the NC/COM contacts closed when DIN0-11 pin #1 is low.

[DAQ_HRS_523_056]

With polarity jumper #1 in the inverting (1) position, the D1 relay on the PPRLYIO-12 board shall have the NO/COM contacts open when DIN0-11 pin #1 is low.

[DAQ_HRS_523_057]

With polarity jumper #2 in the inverting (1) position, the D2 relay on the PPRLYIO-12 board shall have the NC/COM contacts open when DIN0-11 pin #3 is high.

[DAQ_HRS_523_058]

With polarity jumper #2 in the inverting (1) position, the D2 relay on the PPRLYIO-12 board shall have the NO/COM contacts closed when DIN0-11 pin #3 is high.

[DAQ_HRS_523_059]

With polarity jumper #2 in the inverting (1) position, the D2 relay on the PPRLYIO-12 board shall have the NC/COM contacts closed when DIN0-11 pin #3 is low.

[DAQ_HRS_523_060]

With polarity jumper #2 in the inverting (1) position, the D2 relay on the PPRLYIO-12 board shall have the NO/COM contacts open when DIN0-11 pin #3 is low.

[DAQ_HRS_523_061]

With polarity jumper #3 in the inverting (1) position, the D3 relay on the PPRLYIO-12 board shall have the NC/COM contacts open when DIN0-11 pin #5 is high.

[DAQ_HRS_523_062]

With polarity jumper #3 in the inverting (1) position, the D3 relay on the PPRLYIO-12 board shall have the NO/COM contacts closed when DIN0-11 pin #5 is high.

[DAQ_HRS_523_063]

With polarity jumper #3 in the inverting (1) position, the D3 relay on the PPRLYIO-12 board shall have the NC/COM contacts closed when DIN0-11 pin #5 is low.

[DAQ_HRS_523_064]

With polarity jumper #3 in the inverting (1) position, the D3 relay on the PPRLYIO-12 board shall have the NO/COM contacts open when DIN0-11 pin #5 is low.

[DAQ_HRS_523_065]

With polarity jumper #4 in the inverting (1) position, the D4 relay on the PPRLYIO-12 board shall have the NC/COM contacts open when DIN0-11 pin #7 is high.

[DAQ_HRS_523_066]

With polarity jumper #4 in the inverting (1) position, the D4 relay on the PPRLYIO-12 board shall have the NO/COM contacts closed when DIN0-11 pin #7 is high.

[DAQ_HRS_523_067]

With polarity jumper #4 in the inverting (1) position, the D4 relay on the PPRLYIO-12 board shall have the NC/COM contacts closed when DIN0-11 pin #7 is low.

[DAQ_HRS_523_068]

With polarity jumper #4 in the inverting (1) position, the D4 relay on the PPRLYIO-12 board shall have the NO/COM contacts open when DIN0-11 pin #7 is low.

[DAQ_HRS_523_069]

With polarity jumper #5 in the inverting (1) position, the D5 relay on the PPRLYIO-12 board shall have the NC/COM contacts open when DIN0-11 pin #9 is high.

[DAQ_HRS_523_070]

With polarity jumper #5 in the inverting (1) position, the D5 relay on the PPRLYIO-12 board shall have the NO/COM contacts closed when DIN0-11 pin #9 is high.

[DAQ_HRS_523_071]

With polarity jumper #5 in the inverting (1) position, the D5 relay on the PPRLYIO-12 board shall have the NC/COM contacts closed when DIN0-11 pin #9 is low.

[DAQ_HRS_523_072]

With polarity jumper #5 in the inverting (1) position, the D5 relay on the PPRLYIO-12 board shall have the NO/COM contacts open when DIN0-11 pin #9 is low.

[DAQ_HRS_523_073]

With polarity jumper #6 in the inverting (1) position, the D6 relay on the PPRLYIO-12 board shall have the NC/COM contacts open when DIN0-11 pin #11 is high.

[DAQ_HRS_523_074]

With polarity jumper #6 in the inverting (1) position, the D6 relay on the PPRLYIO-12 board shall have the NO/COM contacts closed when DIN0-11 pin #11 is high.

[DAQ_HRS_523_075]

With polarity jumper #6 in the inverting (1) position, the D6 relay on the PPRLYIO-12 board shall have the NC/COM contacts closed when DIN0-11 pin #11 is low.

[DAQ_HRS_523_076]

With polarity jumper #6 in the inverting (1) position, the D6 relay on the PPRLYIO-12 board shall have the NO/COM contacts open when DIN0-11 pin #11 is low.

[DAQ_HRS_523_077]

With polarity jumper #7 in the inverting (1) position, the D7 relay on the PPRLYIO-12 board shall have the NC/COM contacts open when DIN0-11 pin #13 is high.

[DAQ_HRS_523_078]

With polarity jumper #7 in the inverting (1) position, the D7 relay on the PPRLYIO-12 board shall have the NO/COM contacts closed when DIN0-11 pin #13 is high.

[DAQ_HRS_523_079]

With polarity jumper #7 in the inverting (1) position, the D7 relay on the PPRLYIO-12 board shall have the NC/COM contacts closed when DIN0-11 pin #13 is low.

[DAQ_HRS_523_080]

With polarity jumper #7 in the inverting (1) position, the D7 relay on the PPRLYIO-12 board shall have the NO/COM contacts open when DIN0-11 pin #13 is low.

[DAQ_HRS_523_081]

With polarity jumper #8 in the inverting (1) position, the D8 relay on the PPRLYIO-12 board shall have the NC/COM contacts open when DIN0-11 pin #15 is high.

[DAQ_HRS_523_082]

With polarity jumper #8 in the inverting (1) position, the D8 relay on the PPRLYIO-12 board shall have the NO/COM contacts closed when DIN0-11 pin #15 is high.

[DAQ_HRS_523_083]

With polarity jumper #8 in the inverting (1) position, the D8 relay on the PPRLYIO-12 board shall have the NC/COM contacts closed when DIN0-11 pin #15 is low.

[DAQ_HRS_523_084]

With polarity jumper #8 in the inverting (1) position, the D8 relay on the PPRLYIO-12 board shall have the NO/COM contacts open when DIN0-11 pin #15 is low.

[DAQ_HRS_523_085]

With polarity jumper #9 in the inverting (1) position, the D9 relay on the PPRLYIO-12 board shall have the NC/COM contacts open when DIN0-11 pin #17 is high.

[DAQ_HRS_523_086]

With polarity jumper #9 in the inverting (1) position, the D9 relay on the PPRLYIO-12 board shall have the NO/COM contacts closed when DIN0-11 pin #17 is high.

[DAQ_HRS_523_087]

With polarity jumper #9 in the inverting (1) position, the D9 relay on the PPRLYIO-12 board shall have the NC/COM contacts closed when DIN0-11 pin #17 is low.

[DAQ_HRS_523_088]

With polarity jumper #9 in the inverting (1) position, the D9 relay on the PPRLYIO-12 board shall have the NO/COM contacts open when DIN0-11 pin #17 is low.

[DAQ_HRS_523_089]

With polarity jumper #10 in the inverting (1) position, the D10  relay on the PPRLYIO-12 board shall have the NC/COM contacts open when DIN0-11 pin #19 is high.

[DAQ_HRS_523_090]

With polarity jumper #10 in the inverting (1) position, the D10  relay on the PPRLYIO-12 board shall have the NO/COM contacts closed when DIN0-11 pin #19 is high.

[DAQ_HRS_523_091]

With polarity jumper #10  in the inverting (1) position, the D10 relay on the PPRLYIO-12 board shall have the NC/COM contacts closed when DIN0-11 pin #19 is low.

[DAQ_HRS_523_092]

With polarity jumper #10 in the inverting (1) position, the D10 relay on the PPRLYIO-12 board shall have the NO/COM contacts open when DIN0-11 pin #19 is low.

[DAQ_HRS_523_093]

With polarity jumper #11 in the inverting (1) position, the D11  relay on the PPRLYIO-12 board shall have the NC/COM contacts open when DIN0-11 pin #20 is high.

[DAQ_HRS_523_094]

With polarity jumper #11 in the inverting (1) position, the D11  relay on the PPRLYIO-12 board shall have the NO/COM contacts closed when DIN0-11 pin #20 is high.

[DAQ_HRS_523_095]

With polarity jumper #11  in the inverting (1) position, the D11 relay on the PPRLYIO-12 board shall have the NC/COM contacts closed when DIN0-11 pin #20 is low.

[DAQ_HRS_523_096]

With polarity jumper #11 in the inverting (1) position, the D11 relay on the PPRLYIO-12 board shall have the NO/COM contacts open when DIN0-11 pin #20 is low.

#### PPRELAY12 NC Optional

[DAQ_HRS_524_000]

The PPRlyio-12 board shall provide the option of using SPST relays (with NO/COM connections only) by swapping relays and substituting two-terminal connections in place of the three-terminal connections.

#### PPRELAY12 Output Control

[DAQ_HRS_525_000]

The PPRlyio-12 board shall buffer (and possibly invert, depending on the state of the corresponding polarity jumper setting) the input signal on each DIN0-11 pin and pass it through to the corresponding DOUT0-11 pin.

#### PPRELAY12 D0 Output Pin (active high)

[DAQ_HRS_525_001]

The PPRlyio-12 DOUT0-11 header, pin 2 (D0) shall reflect the current state of the DIN0-11 header, pin 2 (D0) if the polarity is jumpered for active high.

#### PPRELAY12 D0 Output Pin (active low)

[DAQ_HRS_525_002]

The PPRlyio-12 DOUT0-11 header, pin 2 (D0) shall reflect the inverted state of the DIN0-11 header, pin 2 (D0) if the polarity is jumpered for active low.

#### PPRELAY12 D1 Output Pin (active high)

[DAQ_HRS_525_003]

The PPRlyio-12 DOUT0-11 header, pin 1 (D1) shall reflect the current state of the DIN0-11 header, pin 1 (D1) if the polarity is jumpered for active high.

#### PPRELAY12 D1 Output Pin (active low)

[DAQ_HRS_525_004]

The PPRlyio-12 DOUT0-11 header, pin 1 (D1) shall reflect the inverted state of the DIN0-11 header, pin 1 (D1) if the polarity is jumpered for active low.

#### PPRELAY12 D2 Output Pin (active high)

[DAQ_HRS_525_005]

The PPRlyio-12 DOUT0-11 header, pin 3 (D2) shall reflect the current state of the DIN0-11 header, pin 3 (D2) if the polarity is jumpered for active high.

#### PPRELAY12 D2 Output Pin (active low)

[DAQ_HRS_525_006]

The PPRlyio-12 DOUT0-11 header, pin 3 (D2) shall reflect the inverted state of the DIN0-11 header, pin 3 (D2) if the polarity is jumpered for active low.

#### PPRELAY12 D3 Output Pin (active high)

[DAQ_HRS_525_007]

The PPRlyio-12 DOUT0-11 header, pin 5 (D3) shall reflect the current state of the DIN0-11 header, pin 5 (D3) if the polarity is jumpered for active high.

#### PPRELAY12 D3 Output Pin (active low)

[DAQ_HRS_525_008]

The PPRlyio-12 DOUT0-11 header, pin 5 (D3) shall reflect the inverted state of the DIN0-11 header, pin 5 (D3) if the polarity is jumpered for active low.

#### PPRELAY12 D4 Output Pin (active high)

[DAQ_HRS_525_009]

The PPRlyio-12 DOUT0-11 header, pin 7 (D4) shall reflect the current state of the DIN0-11 header, pin 7 (D4) if the polarity is jumpered for active high.

#### PPRELAY12 D4 Output Pin (active low)

[DAQ_HRS_525_010]

The PPRlyio-12 DOUT0-11 header, pin 7 (D4) shall reflect the inverted state of the DIN0-11 header, pin 7 (D4) if the polarity is jumpered for active low.

#### PPRELAY12 D5 Output Pin (active high)

[DAQ_HRS_525_011]

The PPRlyio-12 DOUT0-11 header, pin 9 (D5) shall reflect the current state of the DIN0-11 header, pin 9 (D5) if the polarity is jumpered for active high.

#### PPRELAY12 D5 Output Pin (active low)

[DAQ_HRS_525_012]

The PPRlyio-12 DOUT0-11 header, pin 9 (D5) shall reflect the inverted state of the DIN0-11 header, pin 9 (D5) if the polarity is jumpered for active low.

#### PPRELAY12 D6 Output Pin (active high)

[DAQ_HRS_525_013]

The PPRlyio-12 DOUT0-11 header, pin 11 (D6) shall reflect the current state of the DIN0-11 header, pin 11 (D6) if the polarity is jumpered for active high.

#### PPRELAY12 D7 Output Pin (active low)

[DAQ_HRS_525_014]

The PPRlyio-12 DOUT0-11 header, pin 11 (D6) shall reflect the inverted state of the DIN0-11 header, pin 11 (D6) if the polarity is jumpered for active low.

#### PPRELAY12 D7 Output Pin (active high)

[DAQ_HRS_525_015]

The PPRlyio-12 DOUT0-11 header, pin 13 (D7) shall reflect the current state of the DIN0-11 header, pin 13 (D7) if the polarity is jumpered for active high.

#### PPRELAY12 D7 Output Pin (active low)

[DAQ_HRS_525_016]

The PPRlyio-12 DOUT0-11 header, pin 13 (D7) shall reflect the inverted state of the DIN0-11 header, pin 13 (D7) if the polarity is jumpered for active low.

#### PPRELAY12 D8 Output Pin (active high)

[DAQ_HRS_525_017]

The PPRlyio-12 DOUT0-11 header, pin 15 (D8) shall reflect the current state of the DIN0-11 header, pin 15 (D8) if the polarity is jumpered for active high.

#### PPRELAY12 D8 Output Pin (active low)

[DAQ_HRS_525_018]

The PPRlyio-12 DOUT0-11 header, pin 15 (D8) shall reflect the inverted state of the DIN0-11 header, pin 15 (D8) if the polarity is jumpered for active low.

#### PPRELAY12 D9 Output Pin (active high)

[DAQ_HRS_525_019]

The PPRlyio-12 DOUT0-11 header, pin 17 (D9) shall reflect the current state of the DIN0-11 header, pin 17 (D9) if the polarity is jumpered for active high.

#### PPRELAY12 D9 Output Pin (active low)

[DAQ_HRS_525_020]

The PPRlyio-12 DOUT0-11 header, pin 17 (D9) shall reflect the inverted state of the DIN0-11 header, pin 17 (D9) if the polarity is jumpered for active low.

#### PPRELAY12 D10 Output Pin (active high)

[DAQ_HRS_525_021]

The PPRlyio-12 DOUT0-11 header, pin 19 (D10) shall reflect the current state of the DIN0-11 header, pin 19 (D10) if the polarity is jumpered for active high.

#### PPRELAY12 D10 Output Pin (active low)

[DAQ_HRS_525_022]

The PPRlyio-12 DOUT0-11 header, pin 19 (D10) shall reflect the inverted state of the DIN0-11 header, pin 19 (D10) if the polarity is jumpered for active low.

#### PPRELAY12 D11 Output Pin (active high)

[DAQ_HRS_525_023]

The PPRlyio-12 DOUT0-11 header, pin 20 (D11) shall reflect the current state of the DIN0-11 header, pin 20 (D11) if the polarity is jumpered for active high.

#### PPRELAY12 D11 Output Pin (active low)

[DAQ_HRS_525_024]

The PPRlyio-12 DOUT0-11 header, pin 20 (D11) shall reflect the inverted state of the DIN0-11 header, pin 20 (D11) if the polarity is jumpered for active low.

### PPAC420 4-20mA Analog Input Conditioning Board

#### AC420 Capacity

[DAQ_HRS_550_000]

The PPAC420 board shall provide 8 channels of analog conditioning.

#### AC420 Power Supply Connection

[DAQ_HRS_551_000]

The PPAC420 board shall provide a two-pin screw terminal connector (5mm centers) to accept 5V/Gnd from an external power supply.

#### PPAC420 Power Supply LED

[DAQ_HRS_552_000]

The PPAC420 board shall provide an LED that is illuminated whenever power is applied to the board (+5V).

#### PPAC420 Clean Power Supply

[DAQ_HRS_553_000]

The power supply connected to the PPAC420 shall be a "clean" analog-only power supply that does not power digital boards or other noisy devices.

#### PPAC420 Maximum Input Current Range

[DAQ_HRS_554_000]

Each analog input channel shall accept currents in the range 0-20mA.

#### PPAC420 Output Voltage Range

[DAQ_HRS_555_000]

Each analog channel shall produce single-ended outputs in the range -1.25 to +5V (0V=4mA, 5V=20mA).

#### PPAC420 Analog Input Terminals

[DAQ_HRS_556_000]

The PPAC420 board shall provide 4 two-pin screw terminals to connect a current loop to the inputs on the board.

#### PPAC420 Analog Output Terminals

[DAQ_HRS_557_000]

The PPAC420 board shall provide 4 two-pin screw terminals to connect the output voltage to some external device (such as the PPAC-4).

## System Operations

### Human Factors

#### Boot and Shutdown

[DAQ_HRS_1100_000]

The PPDAQ shall automatically begin operation upon application of power.

#### Module Reset and Initialization

[DAQ_HRS_1101_000]

The system shall reset and initialize each each attached I/O module after a power interruption.

# System Interfaces

## Input Power

### PPDAQ Input Power

[DAQ_HRS_1200_000]

DC power, +5V digital, shall be provided to the PPDAQ (Netburner Interface) module.

### PPAC4 Input Power

[DAQ_HRS_1201_000]

DC power, ±12V clean analog, shall be provided to the PPAC4 (four-channel analog conditioning) module.

### PPAIO16-4 Input Power

[DAQ_HRS_1202_000]

DC power, +5V clean analog, shall be provided to the PPAIO16-5 (16-channel analog input, 4-channel analog output) module.

### PPDIO96 Input Power

[DAQ_HRS_1203_000]

DC power, +5V digital, shall be provided to the PPDIO96 (96-channel digital I/O) module.

### PPOPTO12 Input Power

[DAQ_HRS_1204_000]

DC power, +5V digital, shall be provided to the PPOPTO12 (12-channel optoisolation) module.

### PPRELAY Input Power

[DAQ_HRS_1205_000]

DC power, +5V digital, shall be provided to the PPRELAY12 (12-channel relay) module.

### PPSSR16 Input Power

[DAQ_HRS_1206_000]

DC power, +5V digital, shall be provided to the PPSSR16 (16-channel solid-state relay) module.

### Netburner Input Power

[DAQ_HRS_1207_000]

DC power, +9V digital, shall be provided to the Netburner module.

### Netburner Input Power -- USB

[DAQ_HRS_1208_000]

The Netburner MOD-70 evaluation board shall be configured to take power from the J9 connector (power supply connector) rather than the micro-USB port.

### Ethernet Connection

[DAQ_HRS_1209_000]

The system shall interface to the Ethernet using a standard RJ-45 Ethernet connection.

### RS-232 Serial Connection

[DAQ_HRS_1210_000]

The system shall interface via RS-232 serial using a male DB-9/DTE connection.

### USB Connection

[DAQ_HRS_1211_000]

The system shall interface via USB using a standard USB-B or Micro-USB-B connection.

# Footnotes

MCP23S17 GPIO pin assignments are not a requirement. They are provided here for informational purposes. The requirement is only the pin and bit number correlations.

MCP23S17 GPIO pin assignments are not a requirement. They are provided here for informational purposes. The requirement is only the pin and bit number correlations.

MCP23S17 GPIO pin assignments are not a requirement. They are provided here for informational purposes. The requirement is only the pin and bit number correlations.

MCP23S17 GPIO pin assignments are not a requirement. They are provided here for informational purposes. The requirement is only the pin and bit number correlations.

MCP23S17 GPIO pin assignments are not a requirement. They are provided here for informational purposes. The requirement is only the pin and bit number correlations.

MCP23S17 GPIO pin assignments are not a requirement. They are provided here for informational purposes. The requirement is only the pin and bit number correlations.

MCP23S17 GPIO pin assignments are not a requirement. They are provided here for informational purposes. The requirement is only the pin and bit number correlations.

MCP23S17 GPIO pin assignments are not a requirement. They are provided here for informational purposes. The requirement is only the pin and bit number correlations.